## Slide 1: ECE391 Computer System Engineering Lecture 10
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Linux abstraction of PIC
General interrupt abstractions
Linux interrupt system
  data structures
  handler installation & removal
  invocation
  execution
  tasklets

## Slide 3: Linux Abstraction of PICs
Uses a jump table
  same as vector table (array of function pointers)
Table is hw_irq_controller structure (or struct irq_chip)
  each vector # associated with a table
  table used to interact with appropriate PIC (e.g., 8259A, or Advanced PIC)
human-readable name
startup function
shutdown function
disable function
enable function
(+ several others…)
mask function
mask_ack function
unmask function
Notes: Each inerrupt controlle has the human redable name
Star
Array maps each is mapped to the interrupts point to points to control structure you do not have to know how the PIC works
Iterrupt handler goes through this table tointerruct wit the PIC

## Slide 4: Linux Abstraction of PICs
hw_irq_controller structure definition
  IRQs are #’d 0-15 (correspond to vector # - 0x20)
const char* name;
unsigned int (*startup)(unsigned int irq);
void (*shutdown)(unsigned int irq);
void (*enable)...
void (*disable)...
void (*ack)...
void (*end)...
/* we’ll ignore the others... */
8259A’s human-
readable name is
“XT-PIC”; see
/proc/interrupts
Notes: Jum table use a jum/vector table arrof function pointers build by the compiler
IRQ# 0 to 15 vector number 0x20

## Slide 5: PIC Functions in Jump Table: Explanation
Initially, all 8259A interrupts are masked out using mask on 8259A
startup and shutdown functions
  startup is called when first handler is installed for an interrupt
  shutdown is called after last handler is removed for an interrupt
  both functions change the corresponding mask bit in 8259A implmentaion
Notes: Handler installed for particular IRQ
Interrupt for the Tux controller
Register your driver
When you remove the drive it will shut down and turnfo that interrupt

## Slide 6: PIC Functions in Jump Table: Explanation (cont.)
Example
no 8259 interrupts
startup IRQ0 (add a handler)
shutdown IRQ0 (remove last handler)
IR0 on master allowed
to generate interrupts
IR0 on master prevented from
generating interrupts

## Slide 7: PIC Functions in Jump Table (cont.)
disable/enable functions
  used to support nestable interrupt masking (disable_irq, enable_irq)
disable_irq
disable_irq
enable_irq
enable_irq
  on 8259
    first disable_irq calls jump table disable, which masks interrupt on PIC
    last enable_irq calls jump table enable, which unmasks interrupt on PIC
some
function
another
function
disable/enable
pairs must match!

## Slide 8: PIC Functions in Jump Table (cont.)
ack function
  called at start of interrupt handling to ack receipt of the interrupt
  on 8259 (mask and ack) , masks interrupt on PIC, then sends EOI to PIC
end function
  called at end of interrupt handling
  on 8259, enables interrupt (unmasks it) on PIC

## Slide 9: General Interrupt Abstractions: Interrupt Chaining
Hardware view: 1 interrupt  1 handler
Problems
  may have > 15 devices
  > 1 software routines may want to act in response to device
  examples:
    hotkeys for various functions
    move mouse to lower-right corner to start screen-saver

## Slide 10: General Interrupt Abstractions: Interrupt Chaining (cont.)
One approach
  used by terminate and stay resident (TSR) programs in DOS
  form linked list (chain) of handlers using JMP instructions
  not very clean
    no way to remove self
    unless you’re first in list
  to be fair
    TSR program not designed for removal
IRQ4 vector
IRET
JMP

## Slide 11: General Interrupt Abstractions Interrupt Chaining (cont.)
Solution
  interrupt chaining with linked list data structure
  (not list embedded into code!)
IRQ4 vector
execute list #4
list #4
handler 1
handler 2

## Slide 12: General Interrupt Abstractions: Interrupt Chaining (cont.)
Drawbacks of chaining
  for > 1 device
    must query devices to see if they raised interrupt
    not always possible
  for 1 device
    must avoid stealing data/confusing device
    example
      by sending two characters to serial port
      in response to interrupt declaring port ready for one char.
    another example
      reading mouse location twice
      if device protocol specifies reading once per interrupt

## Slide 13: General Interrupt Abstractions: Soft Interrupts (cont.)
Recall: why support interrupts?
  slow device gets timely attention from fast processor
  processor gets device responses without repeatedly asking for them
A useful concept in software
  example: network encryption/decryption
  packet arrives, given to decrypter
  when decrypter (software program) is done
    want to interrupt program
    to transfer data from packet
  but has no access to INTR pin

## Slide 14: General Interrupt Abstractions: Soft Interrupts (cont.)
Solution
  software-generated (soft) interrupt
  (similarly, but later, signals—user-level soft interrupts)
  runs at priority between program and hard interrupts
  usually generated
    by hard interrupt handlers
    to do work not involving device
Linux version is called tasklets
  used by code provided to you for MP1
  discussed later

## Slide 15: Linux’ Interrupt Data Structures
IRQ descriptor table (irq_desc)
status
chip
action list
lock
disable depth
PIC jump
table
handler
flags
irq
device id
device name
next
data
associated
with
a disk
“disk”
why not static in driver? [may have > 1 of one type]
(code)
(linked list)
struct irqaction
flow handler
[handle_level_irq for 8259]

## Slide 16: Linux’ request_irq (kernel/irq/manage.c)
Add the new action structure to the link list of actions
Upon failure free the action structure
Dynamically allocate
new action structure for linked list of actions
Fill in the new action structure
irq # (0-15 for PIC)
bit vector
pointer to interrupt handler
pointer to device-specific
data
human-readable device name
Notes: Interrup handle three arg: irq#, device pointer (void)*
Return 1 if handeled

## Slide 17: Comments on request_irq – Arguments
  irq – irq # (0-15 for PIC)
  handler – pointer to interrupt handler with following arguments
    irq #
    dev_id pointer (type void*)
    handlers should return 1 if handled, 0 if not
  irqflags – bit vector
    IRQF_SHARED – interrupt chaining is allowed
    IRQF_DISABLED – execute handlers with IF=0
    IRQF_SAMPLE_RANDOM – use device timing as source of random numbers
  devname – human-readable device name (visible in /proc/interrupts)
  dev_id – pointer to device-specific data (returned to handler when called)

## Slide 18: Comments on request_irq (cont.)
Start by checking values (two checks from the shown code)
Dynamically allocate new action structure for linked list of actions
Fill in the new action structure
Try to add it
  using setup_irq
  if call fails, free the action structure

## Slide 19: Linux setup_irq (kernel/irq/manage.c)
Critical section begins
Critical section ends
New action is added at the end of the link list
Startup PIC for this interrupt
Create new /proc/irq/<irq#> directory
Interrupt descriptor
PIC jump table
Add handler subdirectory in /proc/irq/<irq#>/<action name>

## Slide 20: Comments on stup_irq
Start with a couple of sanity checks
If random sampling flag is set
  initialize as source of random numbers
  good random numbers are hard to find!
  devices such as disks can be used because of “random” rotational latency to read data (for example)

## Slide 21: Comments on stup_irq (cont.)
Critical section (most of function)
  blocks other activity on descriptor
  uses irqsave/restore to allow handlers to be added from any context
Note that new action goes at the end of the linked list, not the start
Interrupt chaining only allowed
  if all handlers agree to it
  otherwise only first handler is successfully added

## Slide 22: Comments on stup_irq (cont.)
If this handler is the first
  make sure that PIC jump table has proper default functions
  clear some status flags
  clear any previous software disablement (depth)
  call the PIC startup function
After critical section
  create /proc/irq/<irq#> directory if necessary
  add handler subdirectory in /proc/irq/<irq #>/<action name>

## Slide 23: Linux free_irq (kernel/irq/manage.c)
Find the correct irq descriptor
Critical section begins
Critical section ends
Critical section ends
No more handlers for the IRQ;
you can invoke PIC shutdown
Search for action in list
The “continue” causes the rest of the statement
body in the loop to be skipped.
Remove handler subdirectory in /proc/irq/<irq#>/<action name>
Free the action structure
Notes: Unreister the interrup handler
Device specific data
Synchro
If any is currently executing an interrup let him finish

## Slide 24: Comments on free_irq
Arguments
  irq – irq # (0-15 for PIC)
  dev_id – MUST match pointer value used in request_irq call
Start by checking arguments
Critical section starts to prevent manipulations of descriptor
  blocks interrupt from starting to execute
  (interrupt may already be executing on another processor)

## Slide 25: Comments on free_irq (cont.)
Search for action in list
  based on dev_id pointer
  hence need for matching pointer
  passing NULL dev_id not allowed with chained interrupts
Once found (notice that most of the loop executes exactly once)
  remove the action
  if this action/handler was the last for this interrupt,
    turn on software disablement
    (doing so signals interrupts waiting for descriptor lock to abort once they obtain the lock)
    call the PIC shutdown function

## Slide 26: Comments on free_irq (cont.)
Remove the /proc/irq/<irq #>/<action name> entry
On an SMP
  interrupt may be executing on another processor
  need to wait for it to finish after releasing descriptor lock
Finally, free the action structure