## Slide 1: ECE391 Computer System Engineering Lecture 11
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Linux interrupts
  execution
  soft interrupts (tasklets) in Linux

## Slide 3: Aministrivia
Midterm Exam1
  Date/Time: February 27, 7:00pm
  Location:
  (1) Roger Adams Lab (RAL 116)
  Last names starting with A-M
  (2) Chemistry Annex (CA 112)
  Last names starting with N-Z
Review Session
  Thursday February 27 IN CLASS

## Slide 4: Interrupt Invocation
Why funnel all IRQs into one piece of code(instead of producing one function per IRQ) ?
  kernel code/size versus speed tradeoff
    perhaps no big deal for 16
    keep in mind that you’re saving a tiny number of instructions
    APIC used by most SMPs has 256 vectors
interrupt[4]
PUSHL $0xFFFFFFFB
JMP common_interrupt
IDT
vector
#0x24
save all regs
linkage to C func ESP->EAX (first arg.)
call do_IRQ
JMP ret_from_intr
context switch?
restore all registers
IRET
Saves the IRQ through negative number (-5 in the example)
SAVE_ALL
movl %esp, %eax
Notes: Hardware move you to the interrupt code
Interrupts the arguments are going to registers
Linkage takes us to the do irq which is the C function
Context switch
Time slicing done by the processor
Virtualization of the processor

## Slide 5: Stack on Entry to do_IRQ
Automatically saved by the control unit
After call to do_IRQ
orig_eax
saved by SAVE_ALL
return address for IRET
Notes: Signature for

## Slide 6: Linux do_IRQ arch/i386/kernel/irq.c
fastcall convention used to pass arguments in registers;
reduces the number of memory accesses required for the call
call interrupt flow handler handle_level_irq for all 8259A interrupts
Exit irq context and process softirqs if needed
gets the interrupt number from the orig_eax filed in the regs structure
Increments counter of nested interrupt handlers
Record registers at time of interrupt
Notes: Fastcall macro
EAX points to saved registers (pt_regs)
Processor clears IF when it takes an interrupt
Old IF is FLAGS stored stack on interrupts)

## Slide 7: Interrupt Invocation (cont.)
Signature for do_IRQ
fastcall unsigned int do_IRQ (struct pt_regs* regs);
  fastcall macro in Linux tells gcc to pass args in EAX, EDX, ECX
  EAX points to saved registers (regs argument)
  saved registers already on stack
  note that processor clears IF when it takes an interrupt
  EFLAGS stored by processor include original IF value

## Slide 8: Comments on do_irq
Value pushed by irq-specific code re-converted to find irq #
Start with a sanity check
set_irq_regs calls record registers at time of interrupt
  per-CPU storage

## Slide 9: Comments on do_irq (cont.)
irq_enter / irq_exit
  necessary for proper priority
    e.g., second hard interrupt occurs
    after new interrupt handled, should return to first
    must delay processing of soft interrupts
  irq_exit processes soft interrupts when appropriate

## Slide 10: Comments on do_irq (cont.)
Central component
  call interrupt flow handler
  handle_level_irq for all 8259A interrupts
Return value ignored (probably intended to indicate interrupt handled)

## Slide 11: Linux handle_level_irq kernel/irq/chip.c
Critical section begins
Critical section ends
Critical section ends
Call PIC’s mask_ack function
If interrupt already in progress, do nothing
Atomically decide whether to execute handlers
Set status for execution: in-progress and no longer pending
Handler execution done via handle_IRQ_event
Critical section begins
When done, remove in-progress flag
and unmask on PIC (unless disabled)
Notes: Smp_..id unique identifier for the processor
Mask ack send mask the int and sends EOI
Look the handlers if the IRQ-disable you can do by software mechanism
Software site of disable mechanism
Pending to eventually execute the interrupt
Last disable : it is set when we do software disablement
Other processor may enter the critical section and call disable the IRQ 4 (for example)
Need to check if the int is disable befor we tell PIC to enable this interrupt again

## Slide 12: Comments on handle_level_irq
Critical section starts
  to read descriptor status and action (handler) list
  IF=0 at this point (set by processor when taking interrupt)
Immediately call PIC’s mask_ack function (via a wrapper function)
If interrupt already in progress, do nothing
  Interrupt already re-masked and re-acknowledged on PIC
Remove software replay and autoprobe flags
Kernel statistics track # of interrupts seen (see /proc/interrupts)

## Slide 13: Comments on handle_level_irq (cont.)
Atomically decide whether to execute handlers immediately
  do so if handler defined and not disabled by software
  if not, skip to end
    mark as pending and end interrupt handling
    replayed after last nested enable_irq call
Set status for execution: in-progress, and no longer pending

## Slide 14: Comments on handle_level_irq (cont.)
Handler execution done via handle_IRQ_event
  done without descriptor lock
    allows handlers to use infrastructure
    e.g., enable_irq/disable_irq, request_irq/free_irq
  usually done with IF=1 (changed inside handle_IRQ_event)
    done without descriptor lock
    otherwise this code can deadlock with self
When done, remove in-progress flag and unmask on PIC (unless disabled)

## Slide 15: Linux handle_IRQ_event kernel/irq/handle.c
call translates basically to STI
(local means “on this CPU”)
Walk through list; call each handler
(return value 1 means handled)
Turn interrupts back off (IF=0 / CLI)

## Slide 16: Comments on handle_IRQ_event
Set IF=1 unless the first handler asked to be executed with IF=0
  indicated by IRQF_DISABLED flag
  call translates basically to STI (local means “on this CPU”)
Walk through list
  call each handler
  return value 1 means handled
Generate random numbers if desired
Turn interrupts back off (IF=0 / CLI)

## Slide 17: Summary on Descriptor Flags
IRQ_PENDING—interrupt raised by hardware; waiting to be executed
IRQ_INPROGRESS—some processor is executing handlers
IRQ_DISABLED—interrupt disabled in software; postpone execution
IRQ_REPLAY—software replay of previously postponed execution

## Slide 18: Interrupt Execution
event IF status PIC
(initial state) 1 0 —
take interrupt 0 0 IS (in service)
start do_IRQ 0 0 IS
start handle_level_irq 0 0 IS
PIC mask_ack mask step 0 0 IS+MASK
PIC mask_ack EOI step 0 0 MASK
check DISABLED & INPROGRESS 0 0 MASK
start interrupt 0 INPROG MASK
(in handle_IRQ_event) STI 1 INPROG MASK
disable_irq called by a handler 1 INPROG+DISABLED MASK
enable_irq called by a handler 1 INPROG —

## Slide 19: Interrupt Execution (cont.)
event IF status PIC
take another interrupt! 0 INPROG IS
start do_IRQ 0 INPROG IS
PIC mask_ack mask step 0 INPROG IS+MASK
PIC mask_ack EOI step 0 INPROG MASK
check DISABLED & INPROGRESS 0 INPROG MASK
[end interrupt] IRET from interrupt 1 INPROG MASK
done with handlers; CLI 0 INPROG MASK
check and clear PENDING 0 INPROG MASK
remove INPROGRESS 0 0 MASK
call PIC unmask function 0 0 —
IRET from interrupt 1 0 —

## Slide 20: Soft Interrupts in Linux linux/interrupt.h and kernel/softirq.c
When are soft interrupts executed?
  after a hard interrupt completes
  periodically by a daemon in the kernel
How?
  seven or eight prioritized types, including high and low tasklet priorities
  linked list for each tasklet priority
  run on processor on which interrupt is scheduled
  each handler atomic with respect to itself (only)

## Slide 21: Soft Interrupts in Linux (cont.) linux/interrupt.h and kernel/softirq.c
Declaring a handler
name for tasklet_struct
an unsigned long
DECLARE_TASKLET (name, func, data);
void (*func) (unsigned long);
linked list
TASKLET_STATE_SCHED, TASKLET_STATE_RUN
# of disables
pointer to the tasklet function integer which can be used by the tasklet function
next
state
count
func
data
Notes: Macro used to declare the tasklet
Func is the actual handler

## Slide 22: Tasklet Scheduling
The following two calls schedule a tasklet for execution
void tasklet_schedule (struct tasklet_struct* t);
void tasklet_hi_schedule (struct tasklet_struct* t);
First form
  schedules tasklet at low priority
  on the executing processor
Second form schedules at high priority
Enable and disable calls analogous to hard interrupts (including nesting)
Notes: Schedule for executing the software

## Slide 23: Tasklet Execution
do_softirq call
  checks per-processor bit vector of pending priorities (high, low, etc.)
  executes action for each priority [softirq_vec]
  tasklet_action walks through linked list [tasklet_hi_action walks through high-priority list ]
  repeats up to 10 times or until no softirqs are raised
Notes: At the end of Checks the list of tasklets
If there is bug if the tasklet reexcutes itself
This code may hang the kernel

## Slide 24: Tasklet Execution Atomicity
Two bits in state changed atomically
  TASKLET_STATE_SCHED – tasklet scheduled for execution
  TASKLET_STATE_RUN – tasklet executing on some processor
When scheduling
  set TASKLET_STATE_SCHED atomically
  if already set, schedule call does nothing
Notes: Using atomic variables
Atomicity supported by stat emachine
Two bits in the tasklet state SCHED and RUN
Atomicity only one processor gets to execute the tasklet

## Slide 25: Tasklet Execution Atomicity (cont.)
When executing, for each tasklet in linked list (at either priority)
set TASKLET_STATE_RUN atomically (if already set, stop)
check if tasklet is software disabled (count field)
if so, clear TASKLET_STATE_RUN
leave the tasklet in the linked list for this priority
set the pending bit for this priority
daemon will try again later
clear TASKLET_STATE_SCHED
execute handler
clear TASKLET_STATE_RUN
no
flags
SCHED
schedule
schedule
RUN
execute/step C
execute/step E
execute/step E
execute/
step B (disabled)
RUN+
SCHED
execute/
step A
execution (execute/step D) occurs in lower two states (and execute/step A fails in these states)
Notes: Four state because we have four bits
If you win then the tasklet goes to the link list
Interupt can come can do soft irq
Count filed is not zero this is disable and you should not run it
Tasklet can reschedule itself in state RUN
What is the sched occurs in another state
Why we do not check disable before A?