## Slide 1: ECE391 Computer System Engineering Lecture 15
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
x86 support for VM
  paging
Programs to processes
Task id and linkage
One bit on synchronization
Creating processes/tasks

## Slide 3: Aministrivia
MP3 Teams Posted
MP3 Posted
  Checkpoint 1 due date:
  Tuesday March 18 (Tuesday)

## Slide 4: x86 Paging
Paging is the second level of indirection in x86
Each page of a virtual address space is in one of three states
  doesn’t exist
  exists and is in physical memory
  exists, but is now on the disk rather than in memory

## Slide 5: x86 Paging
We can encode these possibilities as follows using 4B
These 4B are called a page table entry (PTE); a group of them is a page table
Question: if we use 4B for every 4kB, how big is the page table for a single virtual address space?
(4 / 4096)  232 = 4MB too big…
31
0
present in physical memory
11
12
1
leftovers for other uses
4kB-aligned address
1
31
0
not present
1
31 bits to differentiate between blocks
on disk & blocks that don’t exist
0

## Slide 6: x86 Paging
Solution?
  page the page table
  i.e., use a hierarchical structure
The page table is just another 4kB page
  it holds 4096 / 4 = 1024 PTEs
page
page table
present bits
page directory
1
page
present bits
page table
1
Notes: Current stage for the page with 4B

## Slide 7: x86 Paging
What about the page directory?
  given
    232 bytes total (32-bit address space)
    210 PTEs per table
    212 bytes per page
  the page directory needs 232/(210  212) = 210 entries total
  which also fits in one page (and could be paged out to disk, although Linux does not)

## Slide 8: x86 Paging
31
0
21
12
11
directory #
page #
offset
22
4kB page
page table
1
pointers
to pages
(+ access
controls);
4B total
pointers to
page tables
(+ access
controls);
4B total
page directory
1
0
1023
. . .
page directory base register
(PDBR, usually called control register 3, or cr3)

## Slide 9: x86 Paging
To translate a virtual address into a physical address
  start with the PDBR (cr3)
  look up page directory entry (PDE) using the 10 MSb of virtual address
  extract page table address from PDE
  look up page table entry (PTE) using next 10 bits of virtual address
  extract page address from PTE
  use last 12 bits of virtual address as offset into page

## Slide 10: x86 Paging
Way too slow to do on every memory access!
Hence the translation lookaside buffers (TLBs)
  keep translations of first 20 bits around and reuse them
  only walk tables when necessary (in x86, OS manages tables, but hardware walks them)
  TLBs flushed when cr3 is reloaded

## Slide 11: x86 Paging
Remember the 11 free bits in the PTEs?
What should we use them to do?
  protect
  optimize to improve performance
Protect
  User/Supervisor (U/S) page or page table
    User means accessible to anyone (any privilege level)
    Supervisor requires PL < 3 (i.e., MAX (CPL,RPL) < 3)
  Read-Only or Read/Write

## Slide 12: x86 Paging
Optimize
  TLBs must be fast, so you can’t use many (~32 or 64)
  nice if
    some translations are the same for all programs
    bigger translations could be used when possible (e.g., use one translation for 4MB rather than 1024 translations)

## Slide 13: x86 Paging
  x86 supports both
    G flag—global
      TLB not flushed when changing to new program or address space (i.e., when cr3 changes)
      used for kernel pages (in Linux)
    4MB pages
      skip the second level of translation
      indicated by PS (page size) bit in PDE
      PS=1 means that the PDE points directly to a 4MB page
      remaining 22 bits of virtual address used as offset
      x86 provides separate TLBs for 4kB & 4MB translations

## Slide 14: Processor/Programs Virtualization
Virtualization of a program – a process
Contents/info
a continuation (stack, EIP, registers, etc.)
I/O permissions
identification
scheduling info.
memory map (virtualization of memory (already covered))
limits on resource usage
file pointer array
signal behavior and info (user-level interrupts)
authentication info/credentials
filesystem info (e.g., current directory)
today and
next couple
of lectures
next
topic
discussed along
with device drivers
near end of class
not discussed
Notes: Continuation (stack, EIP, registers)
IO permissions (graphics card so the program can interact with the device; device registers to be accessed directly
Identification differentiate the programs
Scheduling info which program should run next
Memory map and resource usage how to point to memory regions
File pointer array (open files, network descriptor) -> device drivers
Signal behavior (user level interrupts)

## Slide 15: x86 Task State Segment
Notes: Hardware support for the programs basically continuation state
TSS register to point to memory segment
One used you need to store them before switching
Trap flag: way for debugging programs
SS and ESP saved values for the user privilege values
SS and ESPs for other levels
Switching to kernel stacks
All registers; ldt reg changes for all programs
Part 2 and three are variable length

## Slide 16: Task State Segment Transparency
TSS contains three parts
  first part is shown in diagram
  second two parts are variable-length
    interrupt redirection (for emulation of earlier ISA generations)
    I/O permission bitmap (for individual ports)
  I/O Map Base Address gives pointer to start of the last part
  Segment limit (in TSS descriptor) defines I/O bitmap length
T field – debug trap flag
  if set, execution stops (exception thrown) when task executes
Notes: Second part
I/O permission bit map
I/O map points to the third part
I/O privileges

## Slide 17: Task State Segment Transparency (cont.)
SS/ESP fields are saved values for user privilege level
  Other privilege levels read from SS2/ESP2, SS1/ESP1, SS0/ESP0
I/O bitmap privilege checking
  IOPL (I/O Privilege Level) specifies level needed for arbitrary access
  if CPL > IOPL
    processor checks I/O bitmap in TSS
    exception generated unless
      bitmap contains enough bits to represent port as a bit
      bit representing port (I/O port for in/out instruction) is set to 1
  Linux keeps only the first 1024 ports in bitmap to conserve space
Notes: 16-bit port space
For every port can this progrm aces this port or not
You may not want to access all the space (8KB)
Therefor this is variable length and the data structure is smaller
Linux allows 1000 I/O ports
Tell about MP3

## Slide 18: How Likely is Unlikely OR Why Correctness is Always More Important
Example: priority inversion
  assume that interrupt handlers are short
  interrupt timing is random
note that Linux sends EOI immediately after starting handler
How likely is priority inversion?
  i.e., an interrupt handler with higher PIC priority runs after a handler with lower PIC priority?
Notes: How likely is unlikely?
Why correctness is always more important than performance
Example of priority inversion
Assume that interrupt handlers are short
And interrupt timing is random
Linux sends EOI immediately after starting the handlers
How likely is that we invert our priorities
Handler with lower priority runs before the handler with higher PIC priority
One analysis the duty cycle Execute the handlers is close to 0
Chance of two interrupts in the same time is close to 0
If it did happen it still 50% chance
The flow is the following
critical section synchronizes interrupts
Critical section can be long
Not written by experts (device driver verification is very important)
Bad code for device
CLI zero interrupts are waiting
Must assume that critical section is short
Two interrupts come together
PIC put the low priority inversion
For desktop does not matter -> no priority
For embedded Linux it may be a problem

## Slide 19: How Likely is Unlikely OR Why Correctness is Always More Important
one analysis
  duty cycle is close to 0
  so the chance of two interrupts at the same time is also close to 0
  if it did happen, around 50% (first to occur runs last)

## Slide 20: How Likely is Unlikely OR Why Correctness is Always More Important
The flaw in that analysis
  critical sections synchronize interrupts!
    chance of occurring at the same time may be high
    if someone writes a long critical section (with IF=0)
  PIC reports high priority first
  so low priority runs first!
argument works only if no one writes a long critical section (ever)!

## Slide 21: Task Identification and Linkage
What is a process/task?
  unit of scheduling in Linux
  also name of data structure (struct task_struct) (see linux/sched.h)
User-level view
  each execution context that can be independently scheduled must have its own process descriptor
  traditional process id (pid, a field in task structure)
  from 1 to 32,767 in Linux, used as task-unique identifier
  tgid (thread group id) plays process id role for multithreaded applications (common id for all threads in process)
  most processes belong to a thread group consisting of a single member
Notes: This a data structure that lives in 8KB at the kernel

## Slide 22: Task Identification and Linkage (cont.)
Kernel view
  kernel must handle many processes at the same time
  keeps two data structures in a single per-process area (8kB)
    thread_info structure (keeps pointer to task structure or process descriptor)
    kernel stack
    both dynamically allocated
  architecture-dependent thread info shares space with kernel stack
Remember: DO NOT USE RECURSION IN THE KERNEL!
thread info
kernel stack
8 kB
Notes: Poi
Note: Linux’ current macro uses a per-CPU global variable GET_THREAD_INFO to obtain the thread info pointer
nter to the task structure

## Slide 23
First MP3 Group Meeting