## Slide 1: ECE391 Computer System Engineering Lecture 16
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Programs to processes
Task identification and linkage
Creating processes/tasks
Scheduling
  Philosophy
  Algorithm
  Data structures
  Code walk through

## Slide 3: Aministrivia
MP3 Teams Posted
MP3 Posted
  Checkpoint 1 due date: Tuesday March 18 (Tuesday)

## Slide 4: x86 Paging
Remember the 11 free bits in the PTEs?
What should we use them to do?
  protect
  optimize to improve performance
Protect
  User/Supervisor (U/S) page or page table
    User means accessible to anyone (any privilege level)
    Supervisor requires PL < 3 (i.e., MAX (CPL,RPL) < 3)
  Read-Only or Read/Write

## Slide 5: x86 Paging
Optimize
  TLBs must be fast, so you can’t use many (~32 or 64)
  nice if
    some translations are the same for all programs
    bigger translations could be used when possible (e.g., use one translation for 4MB rather than 1024 translations)

## Slide 6: x86 Paging
  x86 supports both
    G flag—global
      TLB not flushed when changing to new program or address space (i.e., when cr3 changes)
      used for kernel pages (in Linux)
    4MB pages
      skip the second level of translation
      indicated by PS (page size) bit in PDE
      PS=1 means that the PDE points directly to a 4MB page
      remaining 22 bits of virtual address used as offset
      x86 provides separate TLBs for 4kB & 4MB translations

## Slide 7: Processor/Programs Virtualization
Virtualization of a program – a process
Contents/info
a continuation (stack, EIP, registers, etc.)
I/O permissions
identification
scheduling info.
memory map (virtualization of memory (already covered))
limits on resource usage
file pointer array
signal behavior and info (user-level interrupts)
authentication info/credentials
filesystem info (e.g., current directory)
today and
next couple
of lectures
next
topic
discussed along
with device drivers
near end of class
not discussed
Notes: Continuation (stack, EIP, registers)
IO permissions (graphics card so the program can interact with the device; device registers to be accessed directly
Identification differentiate the programs
Scheduling info which program should run next
Memory map and resource usage how to point to memory regions
File pointer array (open files, network descriptor) -> device drivers
Signal behavior (user level interrupts)

## Slide 8: x86 Task State Segment
Notes: Hardware support for the programs basically continuation state
TSS register to point to memory segment
One used you need to store them before switching
Trap flag: way for debugging programs
SS and ESP saved values for the user privilege values
SS and ESPs for other levels
Switching to kernel stacks
All registers; ldt reg changes for all programs
Part 2 and three are variable length

## Slide 9: Task State Segment Transparency
TSS contains three parts
  first part is shown in diagram
  second two parts are variable-length
    interrupt redirection (for emulation of earlier ISA generations)
    I/O permission bitmap (for individual ports)
  I/O Map Base Address gives pointer to start of the last part
  Segment limit (in TSS descriptor) defines I/O bitmap length
T field – debug trap flag
  if set, execution stops (exception thrown) when task executes
Notes: Second part
I/O permission bit map
I/O map points to the third part
I/O privileges

## Slide 10: Task State Segment Transparency (cont.)
SS/ESP fields are saved values for user privilege level
  Other privilege levels read from SS2/ESP2, SS1/ESP1, SS0/ESP0
I/O bitmap privilege checking
  IOPL (I/O Privilege Level field in EFLAGS register) specifies level needed for arbitrary access
  if CPL > IOPL
    processor checks I/O bitmap in TSS
    exception generated unless
      bitmap contains enough bits to represent port as a bit
      bit representing port (I/O port for in/out instruction) is set to 0
  Linux keeps only the first 1024 ports in bitmap to conserve space
Notes: 16-bit port space
For every port can this progrm aces this port or not
You may not want to access all the space (8KB)
Therefor this is variable length and the data structure is smaller
Linux allows 1000 I/O ports
Tell about MP3

## Slide 11: How Likely is Unlikely OR Why Correctness is Always More Important
Example: priority inversion
  assume that interrupt handlers are short
  interrupt timing is random
note that Linux sends EOI immediately after starting handler
How likely is priority inversion?
  i.e., an interrupt handler with higher PIC priority runs after a handler with lower PIC priority?
Notes: How likely is unlikely?
Why correctness is always more important than performance
Example of priority inversion
Assume that interupt handlesr are short
And interrup timig is random
Linux sends EOI immediately after starting the handlers
How likely is that we invert our priorities
Handler with lower priority runs before the handler with higher PIC priority
One analysis the duty cycle Execute the handlers) is close to 0
Chance of two interrupt in the same time is close to 0
If it did happen it still 50% chance
The flow is the following
critical section synchronizes interrupts
Critical section can be long
Not written by experts (device driver verification is very important)
Bad code for device
CLI zero interrupts are waiting
Must assume that critical section is short
Two interrupts come together
PIC put the low priority inversion
For desktop does not matter -> no priority
For embedded Linux it may be a problem

## Slide 12: How Likely is Unlikely OR Why Correctness is Always More Important
one analysis
  duty cycle is close to 0
  so the chance of two interrupts at the same time is also close to 0
  if it did happen, around 50% (first to occur runs last)

## Slide 13: How Likely is Unlikely OR Why Correctness is Always More Important
The flaw in that analysis
  critical sections synchronize interrupts!
    chance of occurring at the same time may be high
    if someone writes a long critical section (with IF=0)
  PIC reports high priority first
  so low priority runs first!
argument works only if no one writes a long critical section (ever)!

## Slide 14: Task Identification and Linkage
What is a process/task?
  unit of scheduling in Linux
  also name of data structure (struct task_struct) (see linux/sched.h)
User-level view
  each execution context that can be independently scheduled must have its own process descriptor
  traditional process id (pid, a field in task structure/process descriptor)
  from 1 to 32,767 in Linux, used as task-unique identifier
  tgid (thread group id) plays process id role for multithreaded applications (common id for all threads in process)
  most processes belong to a thread group consisting of a single member
Notes: This a data structure that lives in 8KB at the kernel

## Slide 15: Task Identification and Linkage (cont.)
Kernel view
  kernel must handle many processes at the same time
  keeps two data structures in a single per-process area (8kB)
    thread_info structure (keeps pointer to task structure or process descriptor)
    kernel stack
    both dynamically allocated
  architecture-dependent thread info shares space with kernel stack
Remember: DO NOT USE RECURSION IN THE KERNEL!
thread info
kernel stack
8 kB
Notes: Poi
Note: Linux’ current macro uses a per-CPU global variable GET_THREAD_INFO to obtain the thread info pointer
nter to the task structure

## Slide 16: Task Identification and Linkage (cont.)
Task structures
  placed in a cyclic, doubly-linked list
  list starts with sentinel: init_task
    first task created by kernel at boot time
    persists until machine shut down/rebooted
    used for lazy page table updates (discussed later)
init_task
tasks.next
tasks.prev
Notes: Eager do work when you know might be needed
Lazy mechanism wait until the work results are actually needed
(need a mechanism to know when the results are needed)

## Slide 17: Task Identification and Linkage (cont.)
For system calls
  must translate pid to struct pid* (small structure referencing task)
  find_pid (kernel/pid.c) uses a hash table
    map large, sparse space into small, dense space
    O(1) access time if # buckets similar to # of elements (really O(n))
    NOT dynamically grown
  doubly-linked list per bin, but back links only for deletion
  hash function = ((pid * big prime #) >> shift)
pid_hash
(array of
struct pid*)
0
4095
. . .
pidchain.next (*)
pidchain.pprev (**)
bound as small
as 16 on machines
with less memory
Notes: Routine to find pid* does this find_pid
Pid0 Pid 10000 pid 17042
We do not want to make a big array for entire 16-bit space
O(1) access time if the number of buckets is similar to the number of elements
Not dynamically grown in the kernel
Shift to take higher bits only
On linux 4000 bins
Set a shift to take something like a random number
For embedded systems this can be small as 16 entries
Each of the bin you will have a doubly-inked list of tasks with the same hash
Back links only used for deletion
finds the task when moving from the user to the kernel space

## Slide 18: Task Identification and Linkage (cont.)
Parent/child relationships
  a process that creates a second process
  is said to be the latter’s parent
  example
    shell from which you run program
    is the parent for those programs
  a tree relationship with unbounded degree
  root of the tree is the init_task
How can such a structure be contained in constant space per node?

## Slide 19: Task Identification and Linkage (cont.)
Include list of children as part of each child’s structure…
parent parent pointer
children.next oldest child pointer
children.prev youngest child pointer
sibling.prev older sibling pointer
sibling.next younger sibling pointer
real_parent original parent (for debugging)
oldest child
parent
younger sibling
older sibling

## Slide 20: Creating Processes/Tasks
User-level: fork, vfork, and clone system calls
In kernel: all map into do_fork
  prototype in linux/sched.h; implementation in kernel/fork.c
int do_fork (unsigned long clone_flags,
unsigned long stack_start,
struct pt_regs* regs,
unsigned long stack_size,
int __user* parent_tidptr,
int __user* child_tidptr);
  __user means not to be dereferenced
  returns new pid or negative value on error
Notes: Fork makes copy of the program in different address space; may take a long time
Each page has R/W two programs can share the physical page wne they only read
Copy the page table but not pages as long th epages are read only we are fine
Most of th epages you do not write you will read
Use the mechanism called copy on write (lazy copy of pages on fork)
Clone creates a new thread the threat shares the address space (new continuationbut same memory space)
They all map into do_fork
-- point to the user code pointers you should not trust them

## Slide 21: Creating Processes/Tasks (cont.)
Parameters
  clone_flags – control flags, to be discussed later; for now, just CLONE_PARENT, which creates a sibling task (like a thread) instead of a child task
  stack_start – the new task’s ESP (in user space; 0 for kernel threads)
  regs – register values for the new task
  stack_size – ignored on x86, but needed on some ISAs
  parent/child_tidptr – filled in as part of system call (sys_clone only)
Notes: One of the registers is the EIP

## Slide 22: Creating Processes/Tasks (cont.)
do_fork calls copy_process (same file) to set up the process descriptor and any other kernel data structures necessary for child execution
  mostly relies on an architecture-dependent version, copy_thread (see arch/i386/kernel/process.c)
  only stack_start and regs are used by x86 version

## Slide 23: Creating Kernel Threads
What is a kernel thread?
  a task without an associated address space
  inherits address space from last user task to execute
  (all address spaces map the kernel pages and data structures)
The interface
  prototype in asm/processor.h; implementation in arch/i386/kernel/process.c
int kernel_thread (int (*fn)(void*), void* arg,
unsigned long flags);
  returns new pid or negative value on error
Notes: MT2 Two weeks from Thursday
Kernel memory is visible to all th eprograms
Kernel threads see only the kernel pages no user level ddres space
Uses the mapping of the last user prgram to touch the kernel pages
To identify kernel thread check the memory mapo
Man memory map own by the tsak and active mem the tsak is currentl using thsese two are idnetical for user task and for kernel mm is NULL