## Slide 1: ECE391 Computer System Engineering Lecture 18
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Scheduling
  general algorithm
  data structures
  code walkthrough

## Slide 3: Aministrivia
MP3 CP2 – Tuesday, April 1

## Slide 4: General Scheduling Algorithm Used by Linux
Time broken into epochs
  each task given a quantum of time (in ticks of 10 milliseconds)
  run until no runnable task has time left
  then start a new epoch
Real-time jobs
  always given priority over non-real-time jobs
  prioritized amongst themselves
Static and dynamic priorities used for non-real-time jobs
Notes: Static priorities for all programs is set to 0

## Slide 5: General Scheduling Algorithm Used by Linux (cont.)
Interactive jobs handled with heuristics
  heuristic estimate job interactiveness
  an interactive job
    can continue to run after running out of time
    takes turns with other interactive jobs
  philosophy is that they don’t usually use up quantum
  heuristic ensures that job can’t use lots of CPU and still be “interactive”
Notes: Heuristic a mechanism which work for addressing certain task
There is not specific mathematic behind to show/prove that this works

## Slide 6: Task State (fields of task_t)
State field can be one of
  TASK_RUNNING
    task is executing currently or waiting to execute
    task is in a run queue on some processor
  TASK_INTERRUPTIBLE
    task is sleeping on a semaphore/condition/signal
    task is in a wait queue
    can be made runnable by delivery of signal
  TASK_UNINTERRUPTIBLE
    task is busy with something that can’t be stopped
    e.g., a device that will stay in unrecoverable state without further task interaction
    cannot be made runnable by delivery of signal

## Slide 7: Task State (fields of task_t) (cont.)
  TASK_STOPPED
    task is stopped
    task is not in a queue; must be woken by signal
  TASK_ZOMBIE
    task has terminated
    task state retained until parent collects exit status information
    task is not in a queue
The swapper process is always runnable (it’s an idle loop)
Notes: There is a return status on each program
It goes to the parent it can ask the status od the child

## Slide 8: Changing the State of a Task
The approaches that do not include memory barriers; compiler may reorder with surrounding code
task->state = (value); // or…
current->state = (value);
Macros that include memory barriers to prevent reordering
set_task_state (task, value); // or…
set_current_state (value);
Notes: The problem is that it can be interrupted
Current make change and than write some other task
Compiler can move it around
How the operation change in the memory
Couple of macros to ensure that you do not move around the state changes on this critical data structures
Things happen in the order you write them
This requires embedded inline assembly

## Slide 9: Scheduling Data Structures
Each processor has a run queue (struct runqueue in sched.c)
  each run queue has two priority arrays
  arrays are lists of tasks of each priority
  they are double-buffered to implement epochs
load bal. for SMPs
expired array
priority array #1
priority array #2
idle task
active array
current task
timestamp
# runnable
lock
# switches
tasks
two pointers used to
implement double-buffering
for priority arrays
for interactive jobs
Notes: Process is sitting in one of the processors all on CPU 0 they will share this one
Must be code to still work by an idle core by other cores and there are mechanism to do
Running the same job on the same processor gives the performance benefit
TLBs and caches
Better to run on a same CPU
However you need to think about load balancing
High performance computing
Programmers know how many processor we have
We can pin a program to a processor
It is particularly important on HPC systems

## Slide 10: Priority Array Structure (struct prio_array in sched.c)
100 real-time priorities
40 regular priorities
One list per priority and a bitmap to make finding non-empty list fast
bitmap of non-empty lists
# active
…
140 doubly-linked lists of tasks
(using task’s run_list field)
Notes: Find first bit in the bit map which is not zero

## Slide 11: Other fields in process descriptor used by the scheduler
Some other task fields used by the scheduler
  TIF_NEED_RESCHED – a flag in thread info (replaced need_resched)
  policy
    SCHED_NORMAL – normal task priority (non-real-time)
    SCHED_FIFO – real-time; retain CPU until preempted or yields
    SCHED_RR – real-time; take turns with tasks at same priority
  rt_priority – real-time priority (static); 0 for normal process
  time_slice – ticks until quantum expires
  static_prio – used to determine quantum (prio is dynamic)
Notes: TIF_NEED_RESCHED current program should be reconsidered when you go to the user space

## Slide 12: Other fields in process descriptor used by the scheduler (cont.)
  cpus_allowed – bitmask of CPUs on which task can execute
  array – current prio_array in which task is scheduled
  last_ran – nanoseconds since last tick/context switch
  sched_time – nanoseconds spent on a processor
  sleep_avg – used for interactive heuristic
  run_list – pointers to next and previous elements in the run queue list to which the process belongs

## Slide 13: Rescheduling and Yielding
Task can change (called a context switch) when
  current task yields by calling schedule (sched_yield at user level)
  current task runs out of time
Other places where a task may yield implicitly
  semaphores
  wake_up_process
  copy_to/from_user
At every timer tick (interrupt, generated every 10 milliseconds)
  run a function (scheduler_tick) to reduce current task’s time
  executes with IF=0
  replace it with another task if appropriate
  interrupt is IRQ0

## Slide 14: Linux Scheduler scheduler_tick and task_running_tick (kernel/sched.c)
update_cpu_clock tracks nanoseconds since last tick/context switch
for all but idle task, call task_running_tick
idle_cpu returns 1 if CPU is running the idle task
Take care of task which already expired
Handle real-time tasks
Critical section begins
Critical section ends
if a task’s time slice expires
dequeue and reschedule the task
breaks long time slices into pieces
Notes: If you are FIFO you will stay on the processor
Long time slices break it into smaller

## Slide 15: Comments on scheduler_tick function
idle_cpu returns 1 if CPU is running the idle task
update_cpu_clock tracks nanoseconds since last tick/context switch
For all but idle task, call task_running_tick

## Slide 16: Comments on task_running_tick function
If the task has already expired
  make sure that it gets rescheduled on return from interrupt
  by setting TIF_NEED_RESCHED
The remainder is a critical section for the run queue
Next handle real-time tasks
  real-time round-robin tasks take turns by placing themselves at the end of the list of their priority
  otherwise real-time tasks just keep rescheduling (until yield or preemption by higher priority)

## Slide 17: Comments on task_running_tick function
If a task’s time slice expires
  take it out of the run queue
  mark it as needing to be removed from processor
  give it a new time slice
  if it’s an interactive job, and expired tasks are not being starved by interactive ones, put it back into run queue (at end)
  normal tasks go into expired queue
Last block
  breaks long time slices into pieces
  round-robin between tasks at same priority

## Slide 18: Linux Scheduler (Part1) schedule function (kernel/sched.c)
Critical section begins
Sleep timestamp records time at which task leaves CPU
if the task is trying to go to sleep check for receipt of signal
default case removes task from run queue
no tasks are runnable
nothing is left in the active run queue
find the next task to run
- find first no-zero bit in the bitmask of the active set
- take the first task at the list indicataed by that bit
Notes: Schedule can be directly called by your task at the kernel
Run queue is the run queue critical section
Task is trying to put itself into sleep
Some tries to wake it up you do it

## Slide 19: Comments on schedule function
Schedule() function called when processor needs to change to new task
  time has expired for current task, or
  task has voluntarily yielded (by calling this function)
Sleep timestamp records time at which task leaves CPU
Remainder is run queue critical section
If the task is trying to go to sleep
  check for receipt of signal
  handles race condition with sleeping in wait queue
Default case removes task from run queue

## Slide 20: Comments on schedule function (cont.)
If no tasks are runnable
  run the idle task
  reset forced expiration of interactive tasks
If nothing is left in the active run queue
  the epoch is over
  swap the priority arrays
  and reset forced expiration of interactive tasks
Find the next task to run
  find first bit selects the priority
  then take the first task at that priority (linked list)

## Slide 21: Linux Scheduler (Part2) schedule function (kernel/sched.c)
Critical section ends
clear need_resched flag for next time current task is scheduled
Switch if newly selected task is not the current one
call architecture-dependent switch function
Notes: Context switch ISA dependent code to do context switch

## Slide 22: Comments on schedule function (cont.)
This portion of the code implements the actual switch
First clears need_resched flag for next time current task is scheduled
Switch only occurs if newly selected task is not the current one
Switch does two things
  does some accounting
  calls architecture-dependent switch function (context_switch)
Notes: Rather efficient code you want to be fast and do not waste time
Built by Read Had for Linux
It should not take time to arbitrate does not contribute to the work being done
ps -auxw 50 to 100 task running
Would not be good if your scheduler takes 50ms