## Slide 1: ECE391 Computer System Engineering Lecture 2
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Aministrivia
MP0
  due Tuesday 7:00pm
  you can hand in anytime during office hours
  singe-up to hand in by Tuesday 7:00pm
  the staff will call you -> you must hand in when called
Tip
  gcc -S
    compiles C file to assembly
    default file produced <program name>.s
    don’t use with –o

## Slide 3: Introduction and Basics
What is x86? (Intel-32-bit architecture, rather than AMD-64)
  variable-length instruction encoding (1-16 bytes)
  small register set: 8 mostly general-purpose
  32-bit, byte-addressable address space
  complex addressing modes
  many data types supported by hardware
Most modern ISAs (e.g., MIPS, Sparc, PowerPC) differ on most points (except memory)

## Slide 4: Registers
General purpose registers

## Slide 5: Registers
  extended, i.e., 32-bit
  EAX accumulator EIP instruction pointer
  EBX base (of array) EFLAGS flags/condition codes
  ECX count (for loops)
  EDX data (2nd operand)
  ESI source index (string copy)
  EDI destination index
  EBP base pointer (base of stack frame)
  ESP stack pointer
Use % as a prefix for registers in assembly
Other registers: floating-point, MMX, etc. (not discussed in this class)

## Slide 6: Data Types
8-, 16-, 32-bit unsigned and 2’s complement
IEEE single- and double-precision floating point
Intel “extended” f.p. (80-bit)
ASCII strings
Binary-coded decimal

## Slide 7: Memory
Microprocessor addresses a maximum of 2n different memory locations, where n is a number of bits on the address bus
Memory
  x86 supports byte addressable memory
  byte (8 bits) is a basic memory unit
  e.g., when you specify address 24 in memory, you get the entire eight bits
  when the microprocessors address a 16-bit word of memory, two consecutive bytes are accessed

## Slide 8: How are bytes stored to memory?
EAX (4 bytes)
larger addresses
big-endian
(big end first)
little-endian
(little end first)
x86 uses this approach

## Slide 9: x86 Instructions – Basics
Operations, data movement, condition codes, control flow, stack ops, data size conversion
Operations
arithmetic logical shift
ADD AND SHL
SUB OR SAR
NEG NOT SHR
INC XOR ROL
DEC ROR
typically 2-operand instructions (destination and one source are the same)

## Slide 10: Operations – Example
ORL %ECX, %EBX # EBX  EBX OR ECX
destination and first source
second source
data type
(technically optional)
L = long (32b)
W = word (16b)
B = byte (8b)
comment marker
operation

## Slide 11: Immediate Values
$0x_______ hex
$0________ octal
$53 decimal
how big can they get?
  usually up to 32 bits
  larger constants  longer instructions
  length of operand must be encoded, too
answer is NOT EAX  0
instead:
EAX  EAX AND M[0]
(usually crashes)
immediate value marker
1,2, …..9
what does the following instruction do?
ANDL 0, %EAX

## Slide 12: Data Movement: Memory Addressing
Memory operand has this general form
displacement(SR1,SR2,scale)
1,2,4,8 (defaults to 1)
address is: displacement + SR1 + SR2 * scale
any but ESP
any
defaults to 0

## Slide 13: Instructions
MOV src, dst
LEA src, dst
Examples:
MOVW %DX, 0x10(%EBP) # M[EBP + 0x10]  DX
MOVB (%EBX,%ESI,4), %CL # CL  M[EBX + ESI * 4]
immediate, register, or memory reference
register, or memory reference
register only
memory reference only – address stored in dst
(can’t both be memory references)

## Slide 14: Instructions: Examples to Solve
EAX  M[0x10000 + ECX]
[answer] MOVL 0x10000(%ECX), %EAX
M[LABEL]  DI
[answer] MOVW %DI, LABEL
ESI  LABEL + 4 (two ways!)
[answer] MOVL $LABEL + 4, %ESI
LEAL LABEL + 4, %ESI
ESI  LABEL + EAX + 4
[answer] LEAL LABEL + 4(%EAX), %ESI
expression calculated by assembler; instruction holds one displacement value

## Slide 15: Condition Codes (in EFLAGS)
Among others (not mentioned in this class)…
SF: sign flag: result is negative when viewed as
2’s complement data type
ZF: zero flag: result is exactly zero
CF: carry flag: unsigned carry or borrow occurred
(or other, instruction-dependent meaning, e.g., on shifts)
OF: overflow flag: 2’s complement overflow (and other instruction-dependent meanings)
PF: parity flag: even parity in result (even # of 1 bits)

## Slide 16: What Instructions Set Flags (condition codes)?
Not all instructions set flags
Some instructions set some flags!
Use CMP or TEST to set flags:
CMPL %EAX, %EBX # flags (EBX – EAX)
TESTL %EAX, %EBX # flags (EBX AND EAX)
Note that EBX does not change in either case