## Slide 1: ECE391 Computer System Engineering Lecture 20
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Memory allocation interfaces in the kernel
  kmalloc
  slab caches
  vmalloc
  buddy system

## Slide 3: Aministrivia
Midterm Exam2
  Date/Time: April 8, 7:00pm
  Location: (1) Roger Adams Lab (RAL 116)
  Last names starting with A-M
  (2) Chemistry Annex (CA 112)
  Last names starting with N-Z
Please notify us about any conflict by 5:00pm Thursday, April 3
Review Session
  Tuesday April 8 IN CLASS

## Slide 4: Files for Memory Management
headers (all under linux/): gfp.h, slab.h, vmalloc.h, slab_def.h, slub_def.h
sources: mm/slab.c, mm/vmalloc.c
swap-related: mm/swap.c, mm/swapfile.c, mm/page_alloc.c

## Slide 5: Memory Allocation
Overview
  a few small items  kmalloc
  a lot of items, repeatedly  slab cache
  a big, physically contiguous region  free pages
  a big area of virtual memory  vmalloc (not necessarily physically contiguous)
flags/allocation priorities (common to all interfaces)
GFP_ATOMIC does not sleep; succeeds only if request can be satisfied with existing free resources (unlikely for large requests)
“get free pages”
Notes: On slab cache: Co-locate them in memory to page them in and out together
GFP_ATOMIC: why not sleep? For the interrupt handler if every call puts me into sleep; in the interrupt handler I should not sleep;
Why good is the sleep; kernel can clear the memory to satisfy your request;

## Slide 6: Memory Allocation
GFP_KERNEL by kernel, drivers, etc.
GFP_NOFS no file system calls (avoids pushing pages to disk)
GFP_NOIO no I/O operations at all
GFP_USER on behalf of a user (low priority)
__GFP_DMA DMA accessible (low physical addresses on some machines)
__GFP_HIGHMEM high memory (PAE (phys. address extensions) on x86) is acceptable
may sleep to wait for pages
(two underscores)
Notes: ..KERNEL
You may sleep on semaphores
NOIO
USER you do something on behalf of the user
Dev. driver user allocates memory in the kernel it is less important than core kernel activities
A Couple of flags to control which part of mem is used to host the allocated memory
DMA can move data in the system without use of the processor; for example network card;
put the next packet and DMA engine on the net. card can copy to the host memory
When you design DMA you want to make them simple and small; DMA cannot generate all the address bits for the mem address
let say only the low part of memory (20 bits) so the allocated memory must be in the right place in memory;
DAM flag says allocate memory in the memory to be DMA accessible
HIGHMEM specific to x86 ; PAE 36 bit extension on physical memory 68 GB of memory but every program can still use only 4GB

## Slide 7: Basic Interface
void* kmalloc (size_t size, gfp_t flags);
  uses exponentially-sized slab caches (to be discussed)
    ranging from 8B to several MB
    up to 4MB in our kernel
  each allocation is contiguous in physical memory
Notes: Takes a bit vector of the flags
Slab cache for 64 byte size, 32 bytes size etc.
Device need usually contiguous memory of physical addresses
void kfree (void*ptr)
User level programs to do similar programs to do malloc things of certain objects
Link them together with link list and use
It was faster than using malloc
Also the objects were close together in memory and faster to search
In kernel you allocate the page and grab the objects from this page

## Slide 8: Basic Interface
Managing a private cache of objects (slab cache)
  frequent allocations/deallocations
  one cache per item type
  physical memory is contiguous
  protocol
    Creation returns a page handle
    Use handle to allocate/deallocate objects or to destroy the slab cache when done
Notes: Takes a bit vector of the flags
Slab cache for 64 byte size, 32 bytes size etc.
Device need usually contiguous memory of physical addresses
void kfree (void*ptr)
User level programs to do similar programs to do malloc things of certain objects
Link them together with link list and use
It was faster than using malloc
Also the objects were close together in memory and faster to search
In kernel you allocate the page and grab the objects from this page

## Slide 9: Basic Interface
kmem_cache* kmem_cache_create (const char* name,
size_t size, size_t align, unsigned long flags,
void (*constructor) (void*, kmem_cache*, unsigned long ignored),
void (*ignored)([same as constructor]));
  name used to avoid >1 cache for same structure
  size is object size; cache grows/shrinks automatically
  alignment specified for individual objects
macro for creation
kmem_cache_t* KMEM_CACHE (<structure>, flags);
Notes: Alignment for individual objects (e.e, 64 byte object page aligned; but not recommended)
Two function pointers
Constructor -
Destructor – is not used
There is a macro to create for you the slab cache
KMEM_CACHE(<structure>, flags);

## Slide 10: Flags for slab cache allocation
  SLAB_HWCACHE_ALIGN align objects to cache lines (makes accesses a little faster)
  SLAB_CACHE_DMA use DMA-accessible memory
  SLAB_POISON fill new memory with 0xA5A5A5A5
  SLAB_RED_ZONE bound objects with “red zones” (test buffer overruns)
Slab cache constructor function
  Callback function used when memory is allocated for the slab cache
  called for each object in new slab
  NOT called for each object allocation (kmem_cache_alloc)
  third argument used to be flags (now always 0)
Notes: Objects aligned on the cache lines;
Cache lines may be different length in microarchitecture therefore we cannot do this using the alignment argument in the API
POISON avoid the case that new object is fill with zeros; you should remember to initialize the allocated memory; you should do initialize the things
RED_ZONE memory management techniques; to test overruns (memory fences)
Constructor is not the same as in C++
Called when memory allocated for slab cache
(Once on each object in new slab)
New page needs to be allocated;

## Slide 11: Slab cache API
Slab cache allocation/deallocation and destruction
void* kmem_cache_alloc (kmem_cache*, gfp_t flags);
void* kmem_cache_zalloc (kmem_cache*, gfp_t flags);
  flags are passed to lower allocator (kmalloc) iff a new slab is allocated
  zalloc version zeroes memory in new object
void kmem_cache_free (kmem_cache*, void*);

## Slide 12: Slab cache API
void kmem_cache_destroy (kmem_cache*);
  fails silently (logs error message) if not empty
int kmem_cache_shrink (kmem_cache*);
  frees empty slabs; returns 0 if all slabs released
Notes: Mechanism to reclaim pages is lazy
Let this object sit in the kernel empty I will allow to use it
kmem_cache* is a slab handle

## Slide 13: Getting big chunks of memory
  multiples of page size (4kB on x86; ISA-dependent)
  physically contiguous
unsigned long get_zeroed_page (gfp_t flags);
unsigned long __get_free_page (gfp_t flags);
unsigned long __get_free_pages (gfp_t flags, unsigned int order);
  flags are same as for kmalloc
  order is log (base 2) of number of pages requested
  (the latter two function names start with two underscores)

## Slide 14: Getting big chunks of memory
void free_page (unsigned long);
void free_pages (unsigned long, int order);
  order must match value used when allocated!
  These functions do not check for you!

## Slide 15: Getting big chunks of memory
Virtual memory allocation (request size in bytes, but allocates pages)
  all functions return virtual addresses
  but all other functions discussed today allocate physically contiguous regions
  what if we don’t care (or need a bigger region)?
  use vmalloc (see linux/vmalloc.h)
void* vmalloc (unsigned long size);
void vfree (void* addr);
Notes: Not necessary physically contiguous
Mapped into pages tables dynamically
Initially in the init_mm
User level and kernel level allocator
Some memory I need give me it
From the memory 178 bytes
Return pointer using mallock
Let me give it back and I call free
How big is this thing?
In practice rather 178 to make it 256 bytes
Let make it easy I put a note this is 256 bytes
Some structure of a fixed size
The header takes and tell me how large it is
The allocator is very fast
This is done in the user space
In kernel I wan to allocate a page
I do not want to use the entire page for the header
and the buddy system allows you to do this.

## Slide 16: The Buddy System
Problem: how to implement memory allocation inside the kernel
  need page alignment for allocations
  may need contiguous regions of physical memory
  need flexible allocation granularity
  want to avoid always rewriting page tables
  can’t easily add information to allocated (physical) memory chunks

## Slide 17: The Buddy System
zone memory map
free lists
1 page
512 pages
4kB to 2MB
. . .
partially busy pair
bitmaps
. . .
total of 1 bit per pair (two buddy blocks)

## Slide 18: The Buddy System
Traditional simple answer
  exponential bins: 1 page, 2 pages, 4 pages, etc.
  buddy system extends with dynamic motion between bins
Partially busy bit: 1 if exactly one buddy in use (0 if both/neither in use)
Example using one group of eight pages
  view also as two groups of four, four groups of two, or eight single pages
  initially appears as a single chunk in 8-page free list
  all other free lists are empty
  all partially free bits are 0

## Slide 19: Buddy system example
Initial configuration
Allocation
  try the correct size free list
  if empty, try the next larger size and break up a chunk
partially busy pair
bitmaps
0
0
0
0
0
0
0
free lists
1 page
2 pages
4 pages
8 pages
an 8-page chunk

## Slide 20: Buddy system example
Request one page of order 0 (order is log of # of pages, i.e., one page here)
  any in free list 0 (1 page)? no…
  any in free list 1 (2 pages)? no…
  any in free list 2 (4 pages)? no…
  any in free list 3 (8 pages)? yes! split it up recursively…

## Slide 21: Buddy system example
partially busy pair
bitmaps
free lists
1 page
2 pages
4 pages
8 pages
0
0
0
1
0
1
1
(allocated page)
free list 0 entry
free list 1 entry
free list 2 entry

## Slide 22: Buddy system example
  Deallocation
    check if buddy is free (is pair bit = 1?)
    if both free, merge and check again (recursively)
  initial configuration for free example
partially busy pair
bitmaps
0
1
0
0
1
0
1
(allocated page)
free list 0 entry
free list 1 entry
free list 2 entry

## Slide 23: Buddy system example
Free element (order is 0)
  check (& flip) buddy bit in order 0
  buddy was free  remove buddy from free list and merge (address remains the same for now)
  check (& flip) buddy bit in order 1
  buddy was free  remove buddy from free list and merge (address changes to start of first 4-page block)
  repeat for order 2, then done; end with initial (all free) configuration

## Slide 24: Memory Zones
Location of zone memory map in 2.6.22.5
One structure to hold all information about contiguous physical pages
  struct pglist_data contig_page_data;
Inside of the page list structure, an array of zone structures
  hold information about each zone (type) of memory
  ZONE_DMA and ZONE_NORMAL for class’ kernel
  struct zone node_zones[MAX_NR_ZONES];

## Slide 25: Memory Zones
Inside each zone structure, an array of free area structures
  these are the exponential bins
  indexed by page order (0 to 10; 4kB to 4MB)
  struct free_area free_area[MAX_ORDER];
Inside each free area structure
  a doubly-linked list of chunks of memory (free_list.prev/next)
  a count of chunks (nr_free)