## Slide 1: ECE391 Computer System Engineering Lecture 3
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Continue x86 instructions
Conditional codes
Control flow instructions
Assembler conventions

## Slide 3: Aministrivia
MP0 due
  extended to tomorrow (Jan. 29) until the end of office hours
PS1 and MP1 are online
CTR-Z stop current job
fg go back to stopped job

## Slide 4: Condition Codes (in EFLAGS)
Among others (not mentioned in this class)…
SF: sign flag: result is negative when viewed as
2’s complement data type
ZF: zero flag: result is exactly zero
CF: carry flag: unsigned carry or borrow occurred
(or other, instruction-dependent meaning, e.g., on shifts)
OF: overflow flag: 2’s complement overflow (and other instruction-dependent meanings)
PF: parity flag: even parity in result (even # of 1 bits)

## Slide 5: What Instructions Set Flags (condition codes)?
Not all instructions set flags
Some instructions set some flags!
Use CMP or TEST to set flags:
CMPL %EAX, %EBX # flags (EBX – EAX)
TESTL %EAX, %EBX # flags (EBX AND EAX)
Note that EBX does not change in either case
What combinations of flags are needed for unsigned/signed relationships comparator?

## Slide 6: Control Flow Instructions (1)
Consider two three-bit values A and B; How to decide if A<B?
#1 #2 #3 #4 #5 #6
A 010 010 010 110 110 110
B -000 -110 -111 -000 -011 -111
C 010 100 011 110 011 111
CF 0 1 1 0 0 1
OF 0 1 0 0 1 0
SF 0 1 0 1 0 1
unsigned < No Yes Yes No No Yes
signed < No No No Yes Yes Yes

## Slide 7: Control Flow Instructions (2)
Note that CF suffices for unsigned <
What about signed < ?
Answer: OF XOR SF
0 | 1 | x | 0
1 | x | 0 | 1
SF
CF/OF
00 01 11 10
0
1

## Slide 8: Control Flow Instructions (3)
Intuition: consider the first bits
A: a ... recall OF = a’bc + ab’c’
B: -b ... SF = c
C: c ...
OF  SF = (a’bc + ab’c’)c’ + (a+b’+c’)(a’+b+c)c
= ab’c’ + ac + b’c
= ab’ + ac + b’c (complementarity (c + c’)
Terms correspond to cases in which A < B
  first term: negative number (a) < non-negative number (b)
  second term: if subtracting from negative number (a) produces negative answer (c), (b) must be larger than (a)
  third term: if subtracting a non-negative number (b) produces a negative answer (c), (b) must be larger than (a)

## Slide 9: Branch Mnemonics
Unsigned comparisons: “above” and “below”
Signed comparisons: “less” and “greater”
Both: equal/zero
unsigned jne jb jbe je jae ja
relationship ≠ < ≤ = ≥ >
signed jne jl jle je jge jg
in general, can add “n” after “j” to negate sense
forms shown are those used when disassembling
  do not expect binary to retain your version
  e.g., “jnae” becomes “jb”

## Slide 10: Other Control Instructions
Other branches
  jo — jump on overflow (OF)
  jp — jump on parity (PF)
  js — jump on sign (SF)
  jmp — unconditional jump
Control instructions: subroutine call and return
CALL printf # (push EIP), EIP  printf
CALL *%EAX # (push EIP), EIP  EAX
CALL *(%EAX) # (push EIP), EIP  M[EAX]
RET # EIP  M[ESP], ESP  ESP + 4

## Slide 11: Stack Operations
Push and pop supported directly by x86 ISA
PUSHL %EAX # M[ESP – 4]  EAX, ESP  ESP – 4
POPL %EBP # EBP  M[ESP], ESP  ESP + 4
PUSHFL # M[ESP – 4]  EFLAGS, ESP  ESP – 4
POPFL # EFLAGS  M[ESP], ESP  ESP + 4

## Slide 12: Data Size Conversion
These instructions extend 8- or 16-bit values to 16- or 32-bit values
General form
MOV
Examples
MOVSBL %AH, %ECX # ECX  sign extend to 32-bit (AH)
MOVZWL 4(%EBP), %EAX # EAX  zero extend to 32-bit (M[EBP + 4])
to type
S—sign extend
Z—zero extend
from type

## Slide 13: Assembler Conventions
label: requires a colon, and is case-sensitive
(unlike almost anything else in assembly)
# comment to end of line
/* C-style comment
… (can consist of multiple lines) */
; command separator (NOT a comment as in LC-3)
.string “Hello, world!”, “me” # NUL-terminated
.byte 100, 0x30, 052 # integer constants of various sizes
.word …
.long …
.quad …
.single … # floating-point constants
.double …
If assembly file name ends in .S (case-sensitive!), file is first passed through C’s preprocessor (#define and #include)