## Slide 1: ECE391 Computer System Engineering Lecture 4
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Code example
Calling convention and stack frames
Application to example
Misc. x86 instructions

## Slide 3: Aministrivia
Prelab 1 due Tuesday
Done with everything you need to know today

## Slide 4: Code Example
Given: EBX pointing to an array of structures with ECX elements in the array
Find: min and max age
first, define registers
  ESI — index into array
  EAX — current age
  EDX — min age seen
  EDI — max age seen
next, use systematic decomposition…
the structure
char* name
long age
find min/max
init vars
loop over
elements
START
END
compare
one age
ESI  ESI + 1
ESI  0
EDX  large #
EDI  small #
ESI ≥
ECX ?
Y
N

## Slide 5: Code Example - Loop Design Process (1)
What is the task to be repeated?
  update the min/max ages
  based on the age of a single person in the array
What are the invariants?
  ESI = array index of person being considered
  EDX = min age of those earlier in array
  EDI = max age of those earlier in array
  ECX = size of array
What are the stopping conditions?
  reach the end of the array
  i.e., ESI ≥ ECX

## Slide 6: Code Example - Loop Design Process (2)
What must be done when a stopping condition is met?
  nothing! (by definition of this particular problem)
How do we prepare for the first iteration?
  set array index to point to first person
  set min age to something large (or to first person’s, but may not exist)
  set max age to something small
How do we prepare for subsequent iterations?
  update min/max age based on current person
  increment ESI

## Slide 7: Code Example - Loop Body
EAX  age
max  EAX
EAX >
max ?
Y
N
(empty)
min  EAX
EAX <
min ?
Y
N
(empty)
compare
one age

## Slide 8: Code Example – Assembly (1)
XORL %ESI,%ESI # init vars
MOVL TWO_MM,%EDX
MOVL TWO_MM+4,%EDI
LOOP:
CMPL %ECX,%ESI # loop test
JGE DONE
# read the age using one memory reference.
MOVL 4(%EBX,%ESI,8),%EAX
CMPL %EDI,%EAX # check the max. age
JLE NOT_MAX
MOVL %EAX,%EDI

## Slide 9: Code Example – Assembly (2)
NOT_MAX:
CMPL %EDX,%EAX # check the min age
JGE NOT_MIN
MOVL %EAX,%EDX
NOT_MIN:
INCL %ESI # loop update
JMP LOOP
DONE: # more code ...
TWO_MM: .LONG 0x7FFFFFFF, 0x80000000

## Slide 10: The Calling Convention (1)
What is a calling convention?
  generally: rules for subroutine interface structure
  specifically
    how information is passed into subroutine
    how information is returned to caller
    who owns registers
  often specified by vendor so that different compilers’ code can work together (it’s a CONVENTION)
Parameters for subroutines
  pushed onto stack
  from right to left in C
  order can be language-dependent

## Slide 11: The Calling Convention (2)
Subroutine return values
  EAX for up to 32 bits
  EDX:EAX for up to 64 bits
  floating-point not discussed
Register ownership
  return values can be clobbered by subroutine: EAX and EDX
  caller-saved: subroutine free to clobber; caller must preserve
    ECX
    EFLAGS
  callee-saved: subroutine must preserve value passed in
    stack structure: ESP and EBP
    other registers: EBX, ESI, and EDI

## Slide 12: Stack Frames in x86 (1)
The call sequence
0. save caller-saved registers (if desired)
1. push arguments onto stack
2. make the call
3. pop arguments off the stack
4. restore caller-saved registers

## Slide 13: Stack Frames in x86 (2)
The callee sequence (creates the stack frame)
0. save old base pointer and get new one
1. save callee-saved registers (always)
2. make space for local variables
3. do the function body
4. tear down stack frame (locals)
5. restore callee-saved registers
6. load old base pointer
7. return

## Slide 14: Stack Frames in x86 (3)
Example of caller code (no caller-saved registers considered)
int func (int A, int B, int C);
func (100, 200, 300);
PUSHL $300
PUSHL $200
PUSHL $100
CALL func
ADDL $12,%ESP
# result in EAX

## Slide 15: Stack Frames in x86 (4)
Example of subroutine code and stack frame creation and teardown
int func (int A, int B, int C)
{
/* 12 bytes of local variables */
…
}
call func (100, 200, 300);

## Slide 16: Stack Frames in x86 (4)
ret. addr
A=100
B=200
C=300
ESP
(old frame)
EBP
stack on entry
to function
ESP
stack during
function body
EBP
ret. addr
A=100
B=200
C=300
old EBP
local
vars.
PUSHL %EBP
MOVL %ESP,%EBP
SUBL $12,%ESP
(body)
LEAVE
RET
ESPEBP+4, EBPM[EBP]

## Slide 17: Subroutine Example Code
Earlier assumptions
  some values start in registers (array pointer in EBX, length in ECX)
  could specify output regs (min. age in EDX, max. age in EDI)
As a C function, we could write…
void find_min_max (person* group, long n_people,
min_max* mm)
char* name
long age
array of
long min
long max

## Slide 18: Subroutine Example Code (cont.)
{ step 1: create the stack frame
  PUSHL %EBP
  MOVL %ESP,%EBP
  PUSHL %EBX # protect callee-saved # registers
  PUSHL %ESI
  PUSHL %EDI
  step 2: link to our input interface
  MOVL 8(%EBP),%EBX # group
  MOVL 12(%EBP),%ECX # n_people
  step 3: insert our code from before
  step 4: link from our output interface
MOVL 16(%EBP),%EBX # load mm into EBX
MOVL %EDX,0(%EBX) # mm->min
MOVL %EDI,4(%EBX) # mm->max
ESP
EBP
(no local vars.)
(EDI)
(ESI)
(EBX)
old EBP
ret. address
group
n_people
mm

## Slide 19: Subroutine Example Code (cont.)
step 5: tear down stack frame
# we have no local variables to remove
# restore callee-saved registers
#(note that order is reversed!)
POPL %EDI
POPL %ESI
POPL %EBX
LEAVE
RET
alternate version (used by gcc)
LEAL -12(%EBP),%ESP
POPL %EDI
POPL %ESI
POPL %EBX
POPL %EBP
RET
ESP
EBP
(no local vars.)
(EDI)
(ESI)
(EBX)
old EBP
ret. address
group
n_people
mm

## Slide 20: Multiplication and Division
MULL %EBX # unsigned EDX:EAX  EAX * EBX
IMULL %EBX # signed (as above)
# multiple-operand forms are ONLY for signed operations
IMULL %ECX,%EBX # signed EBX  EBX * ECX (high bits discarded)
IMULL $20,%EDX,%ECX # signed ECX  20 * EDX (high bits discarded)
DIV %EBX # unsigned EAX  EDX:EAX / EBX
# EDX  remainder
IDIV … # (signed version)

## Slide 21: Data Type Alignment (1)
Memory addresses
  when loading data from or storing data to memory
  use address that is multiple of size of data
Examples
  for bytes, use any address
  for words (16-bit), use even addresses only (multiple of 2 bytes)
  for longs (32-bit), use multiple-of-4 addresses only

## Slide 22: Data Type Alignment (2)
Rationale: simplifies implementation of processor-memory interface
  required by many modern ISAs
  optional on x86 (but very slow if you don’t align)
  x86 has alignment check flag (AC), but usually turned off
Use “.ALIGN 4” (number is an argument) to align x86 assembly
  for x86 assemblers, you can even do so in the middle of code

## Slide 23: Device I/O
How does a processor communicate with devices?
Two possibilities
  independent I/O — use special instructions and a separate I/O port address space
  memory-mapped I/O — use loads/stores and dedicate part of the memory address space to I/O
x86 originally used only independent I/O
  but when used in PC, needed a good interface to video memory
  solution? put card on the bus, claim memory addresses!
  now uses both, although ports are somewhat deprecated

## Slide 24: Device I/O
I/O instructions have not evolved since 8086
  16-bit port space
    byte addressable
    little-endian (looks like memory)
  instructions
IN port, dest.reg
OUT src.reg, port
  the register operands are NOT general-purpose registers
    all data to/from AL, AX, or EAX
    port is either an 8-bit immediate (not 16!) or DX