## Slide 1: ECE391 Computer System Engineering Lecture 5
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
x86 assembly wrap-up
role of system software
system calls, exceptions, & interrupts
processor support for interrupts

## Slide 3: Aministrivia
MP1 Handin and Demo Schedule
Monday 2/10, 7:00pm
  students with last names start with A-G
Tuesday 2/11, 7:00pm
  students with last names start with H-Q
Wednesday 2/12, 7:00pm
  students with last names start with R-Z
You must be present at 7:00pm with an MP1 gradesheet printed in order to handin

## Slide 4: Data Type Alignment (1)
Memory addresses
  when loading data from or storing data to memory
  use address that is multiple of size of data
Examples
  for bytes, use any address
  for words (16-bit), use even addresses only (multiple of 2 bytes)
  for longs (32-bit), use multiple-of-4 addresses only

## Slide 5: Data Type Alignment (2)
Rationale: simplifies implementation of processor-memory interface
  required by many modern ISAs
  optional on x86 (but very slow if you don’t align)
  x86 has alignment check flag (AC), but usually turned off
Use “.ALIGN 4” (number is an argument) to align x86 assembly
  for x86 assemblers, you can even do so in the middle of code

## Slide 6: Device I/O
How does a processor communicate with devices?
Two possibilities
  independent I/O — use special instructions and a separate I/O port address space
  memory-mapped I/O — use loads/stores and dedicate part of the memory address space to I/O
x86 originally used only independent I/O
  but when used in PC, needed a good interface to video memory
  solution? put card on the bus, claim memory addresses!
  now uses both, although ports are somewhat deprecated

## Slide 7: Device I/O
I/O instructions have not evolved since 8086
  16-bit port space
    byte addressable
    little-endian (looks like memory)
  instructions
IN port, dest.reg
OUT src.reg, port
  the register operands are NOT general-purpose registers
    all data to/from AL, AX, or EAX
    port is either an 8-bit immediate (not 16!) or DX

## Slide 8: Role of System Software (1)
System software serves three purposes
  virtualization
  protection
  abstraction (particularly hiding asynchrony)
virtualization:
  the illusion of multiple/practically unlimited resources
protection:
  reduce/eliminate the chance of accidental and/or malicious destruction of data/results by another program

## Slide 9: Role of System Software (2)
abstraction:
  hide fundamentally asynchronous nature of processor/device interaction
  provide simpler and more powerful interfaces (integrated w/protection)
ETH
someone
else’s code
your code
buf
buf
buf
neither can cross
protection boundary

## Slide 10: System Calls, Interrupts, and Exceptions (1)
recall that subroutines allow a programmer to encapsulate common operations
the operating system
  want to provide an interface including common operations
  BUT don’t want to re-link programs
  NOR rely on everyone having exactly the same OS version
CALL
CALL
2
6
4
1
3
5
7

## Slide 11: System Calls, Interrupts, and Exceptions (2)
solution
  add a level of indirection!
with indirection
  to rewrite OS, just change the table
  application code does not change
CALL #1
0
1
2
3
4
called
“handlers”
or “handler
procedures”
table of
function
pointers

## Slide 12: System Calls, Interrupts, and Exceptions (3)
in LC-3, we used the TRAP instruction; in x86, it’s the INT instruction:
INT 8-bit imm. # (PUSH EIP), EIP  table[imm8]
  the RTL is actually a little more complicated, as you’ll see later in course
  called a trap (after instruction, or trap door through protection boundary)
  also called a system call (for operating system)

## Slide 13: System Calls, Interrupts, and Exceptions (4)
vector tables/jump tables
  i.e., tables of function pointers
  convenient abstraction for many procedure-like activities
Question:
  What happens if software does something wrong, e.g.,
    accesses a non-existent memory location?
    issues an illegal/undefined instruction? divides by 0?
What do we do to handle problems?
  state machine that you design for processor may have don’t cares
  state machine that you build will do something (may be unknown)
  so just let it run! (e.g., 6502 did so… and programmers used!)

## Slide 14: System Calls, Interrupts, and Exceptions (5)
a better solution: exceptions!
  processor maps each problem to a vector #
  calls procedure in vector table by #
Where else might we use vector tables?
Consider processor interactions with devices
  a disk access takes about 10 milliseconds
  new machines in lab: 10 ms = 32 million cycles
should processor sit around asking, “Are my data here yet?”

## Slide 15: System Calls, Interrupts, and Exceptions (6)
  analogous to posting a letter to a friend in Europe
  and checking your mailbox every minute for a reply
  instead, have your mail carrier ring your doorbell when it arrives
  in a processor, we call that an interrupt
How can we use a vector table for interrupts?
  each device has a vector #
  call corresponding procedure in vector table when device generates
x86 ISA
  uses one table for all three kinds
  called the Interrupt Descriptor Table (IDT)

## Slide 16: Processor Support for Interrupts (1)
How does a processor support interrupts?
Logically…
N=8 on x86 (and LC-3)
How should we change a processor’s state machine to incorporate interrupts?
INTR
N
which one?

## Slide 17: LC-3 state machine interrupt support

## Slide 18: Processor Support for Interrupts (2)
x86 allows software to block interrupts with a status flag (in EFLAGS)
normal interrupts occur only when the interrupt enable flag (IF) is set
some interrupts are too important
  e.g., memory errors, power warnings, etc.
  these are NOT maskable, and use a separate input to processor
  called non-maskable interrupts (NMI)
INTR
8
which (uses data bus)
NMI
x86

## Slide 19: Interrupt Descriptor Table
as mentioned earlier
  x86 uses a single vector table
  the Interrupt Descriptor Table (IDT)
  hold vectors for interrupts, exceptions, and system calls
note that this picture is partly OS-specific
  the exception vector numbers are specified by Intel – Why?
    A: generated directly by processor’s state machine
  programmable interrupt controller (PIC) will be discussed later;
    range of vectors generated is programmable, and is shown for Linux 2.4
  note that a single entry is used for all system calls in Linux

## Slide 20: Interrupt Descriptor Table

## Slide 21: Shared Data and Resources (1)
The question
  interrupt handlers and programs share resources
    What resources are shared between them?
    How might interactions cause problems?
    What can we do to fix those problems?

## Slide 22: Thought Problem on Shared Resources (2)
Obvious things
  registers
    solution? save them to the stack
  memory
    solution? privatize
    will still need to share some things; discussed later

## Slide 23: Thought Problem on Shared Resources (3)
Less obvious
  condition codes
    solution? again, save them to the stack
  shared data
    For example MP1/real-time clock driver
      shared 4-byte variable holding: interrupt count (high 3 bytes) and last interrupt type (low byte)
      interrupt handler counts interrupts and sets type: type is alarm clock, periodic, or update (1 sec period)
      system call (read)
        reads shared variable
        resets interrupt count to 0

## Slide 24: Thought Problem on Shared Resources (4)
More subtle
  external state (e.g., on devices)
  compiler optimization (e.g., volatility)
  security leaks
    e.g., application waits for interrupt, then observes values written by OS to stack
    solution? use separate stack for kernel