## Slide 1: ECE391 Computer System Engineering Lecture 6
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Shared resources
Critical sections

## Slide 3: Shared Data and Resources (1)
The question
  interrupt handlers and programs share resources
    What resources are shared between them?
    How might interactions cause problems?
    What can we do to fix those problems?

## Slide 4: Thought Problem on Shared Resources (2)
Obvious things
  registers
    solution? save them to the stack
  memory
    solution? privatize
    will still need to share some things; discussed later

## Slide 5: Thought Problem on Shared Resources (3)
Less obvious
  condition codes
    solution? again, save them to the stack
  shared data
    For example MP1/real-time clock driver
      shared 4-byte variable holding: interrupt count (high 3 bytes) and last interrupt type (low byte)
      interrupt handler counts interrupts and sets type: type is alarm clock, periodic, or update (1 sec period)
      system call (read)
        reads shared variable
        resets interrupt count to 0

## Slide 6: Thought Problem on Shared Resources (4)
More subtle
  external state (e.g., on devices)
  compiler optimization (e.g., volatility)
  security leaks
    e.g., application waits for interrupt, then observes values written by OS to stack
    solution? use separate stack for kernel

## Slide 7: Examples of Shared Resources: Example #1: a shared linked list
step 1: old_head = head;
step 2: head = new_elt;
Oops! an interrupt!
step 3: new_elt->next = old_head;
?
old_head
head
new_elt
1
2
3

## Slide 8: Examples of Shared Resources: Example #1: a shared linked list
The problem?
  linked list structure has invariant
  head points to first, chained through last via next field, ends with NULL
  complete operation maintains invariant
  partial operation does not – need atomic update

## Slide 9: Examples of Shared Resources: Example #2: external state
The core problem
  devices have state
  processors interact with devices using specific protocols
  protocol often requires several steps (e.g., I/O instructions)
  device cannot differentiate which piece of code performed an operation
Example:
  VGA controller operations for scrolling window with color modulation
  interrupt handler drives color manipulations
  program handles scrolling using pixel shift
  both use VGA attribute control register (port 0x3C0)

## Slide 10: Examples of Shared Resources: Example #2: external state
Protocol for attribute control register
  22 different attributes accessed via this register
  first send index
  then send data
  VGA tracks whether next byte sent is index or data
Problem: processor can’t know which one is expected
Solution: reading from port 0x3DA forces VGA to expect index next

## Slide 11: Examples of Shared Resources: Example #2: external state
Consider the program code
  the horizontal pixel panning register is register 0x13
  assume that the code should write the value 0x03 to it
(discard)  P[0x3DA] MOVW $0x3DA, %DX
INB (%DX),%AL
0x13  P[0x3C0] MOVW $0x3C0, %DX
MOVB $0x13, %AL
OUTB %AL, (%DX)
0x03  P[0x3C0] MOVB $0x03, %AL
OUTB %AL, (%DX)

## Slide 12: Examples of Shared Resources: Example #2: external state
What happens if the interrupt occurs after the first write to 0x3C0?
  the interrupt handler is executing basically the same code
  leaves the VGA expecting an index
What is the solution?

## Slide 13: Examples of Shared Resources: Example #3: handshake synchronization
A device generates an interrupt after it finishes executing a command
Consider the following attempt to synchronize
the shared variable…
  int device_is_busy = 0;
the interrupt handler…
  device_is_busy = 0;

## Slide 14: Examples of Shared Resources: Example #3: handshake synchronization
The program function used to send a command to the device…
while (device_is_busy);/* wait until device is free */
device_is_busy = 1;
/* send new command to device */
Q: Does the loop work?
No.
  Compiler assumes sequential program.
  Variables can’t change without code that changes them.

## Slide 15: Examples of Shared Resources: Example #3: handshake synchronization
LOOP: MOVL device_is_busy, %EAX
CMPL $0, %EAX
JNE LOOP
Nothing can change variable, so no need to reload (move LOOP down a line).
Now nothing can change EAX, so move it down another line (to branch!).
Will interrupt handler break you out of the resulting infinite loop?

## Slide 16: Examples of Shared Resources: Example #3: handshake synchronization
Solution
  mark variable as volatile
  tells compiler to never assume that it hasn’t changed between uses
Why not mark everything volatile?
  forces compiler to always re-load variables
  more memory operations = slower program

## Slide 17: Examples of Shared Resources: Example #3: handshake synchronization
Is it ok to swap setting the variable and sending the command?
No.
  introduces a race condition:
/* send new command to device */
---- INTERRUPT OCCURS HERE ----
device_is_busy = 1;
    Next command call blocks (forever) for device to be free.

## Slide 18: Examples of Shared Resources: Example #3: handshake synchronization
Unfortunately, writing your code correctly is not enough.
  compiler optimization allowed to reorder
    so long as code is equivalent
    assuming sequential program
  also (and much more subtly!)
    ISA implementation is allowed to reorder
Message
  important to think about reordering possibilities by compiler and ISA and to prevent bad reorderings

## Slide 19: Critical Sections
Some parts of program need to appear to execute atomically, i.e., without interruption
Full version: atomic with respect to code in interrupt handler
  for now, the clause is implied i.e., only interrupt handlers can operate during our programs
  however, multiprocessors may have >1 program executing at same time

## Slide 20: Critical Sections
Solution?
  IF (the interrupt enable flag)
critical section start (CLI)
(the code to be executed atomically)
critical section end (STI)
What else must be prevented?
  no moving memory ops into or out of critical section!

## Slide 21: Critical Sections in Examples
Example #2: external state
MOVW $0x3DA, %DX
INB (%DX),%AL
MOVW $0x3C0, %DX
MOVB $0x13, %AL
OUTB %AL, (%DX)
MOVB $0x03, %AL
OUTB %AL, (%DX)
CLI
STI
the critical section
should be as short
as possible

## Slide 22: Critical Sections in Examples
Why should critical sections be short?
  avoid delaying device service by interrupt handler
  long delays can even crash system (e.g., swap disk driver timeout)
Example #1: a shared linked list
old_head = head;
head = new_elt;
new_elt->next = old_head;
If interrupt handler can change list, too, leaving out first inst. creates race
Example #3: handshake synchronization—volatile suffices for this example
CLI
could skip first statement,
but including is safer
STI

## Slide 23: Critical Sections in Examples
Consider a queue structure
  some structure, thing_t
  the program produces things
  the interrupt handler consumes things

## Slide 24: Critical Sections in Examples
thing_t* dequeue ()
{
thing_t* thing;
if (q_head == q_tail) {
return NULL;
}
thing = q[q_head % 16];
q_head = q_head + 1;
return thing;
}
thing_t* q[16];
unsigned int q_head = 0, q_tail = 0;
void queue_thing (thing_t* new_thing)
{
/* If queue is full, wait. */
while (q_head + 16 == q_tail);
q[q_tail % 16] = new_thing;
q_tail = q_tail + 1;
}

## Slide 25: Critical Sections in Examples
Where should we add critical sections?
  none needed!
  but we do need to make q_head and q_tail volatile
What about program changes?
  e.g., replace
q[q_tail % 16] = new_thing;
q_tail = q_tail + 1;
  with
q[(q_tail++) % 16] = new_thing;

## Slide 26: Critical Sections in Examples
Is the code equivalent?
Does store to q or q_tail happen first?
We removed the intervening load of a volatile variable…