## Slide 1: ECE391 Computer System Engineering Lecture 7
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Queue example
Multiprocessors and locks
Spin locks
Synchronization issues

## Slide 3: Aministrivia
PS2 out
  experience with locks;
  read documentation VGA (video graphic array) needed for your MP2
MP2 soon to be released
Tips: Inside VM you may use
  grep & find to find definitions of functions

## Slide 4: Example of Synchronization: Program
Consider a queue structure
  some structure, thing_t
  the program produces things
  the interrupt handler consumes things
thing_t* q[16];
unsigned int q_head = 0, q_tail = 0;
void queue_thing (thing_t* new_thing)
{
/* If queue is full, wait. */
while ( q_head + 16 == q_tail );
q[q_tail % 16] = new_thing;
q_tail = q_tail + 1;
}
q_head
q_tail

## Slide 5: Example of Synchronization: Interrupt Handler
thing_t* dequeue ()
{
thing_t* thing;
if (q_head == q_tail) {
return NULL;
# you need not to block
}
thing = q[q_head % 16];
q_head = q_head + 1;
return thing;
}
q_head
q_tail
Assumptions
  One interrupt handler that calls dequeue
  Handler does not interrupt itself

## Slide 6: Example of Synchronization: Program
Consider a queue structure
  some structure, thing_t
  the program produces things
  the interrupt handler consumes things
thing_t* q[16];
unsigned int q_head = 0, q_tail = 0;
/* volatile to avoid optimization */
void queue_thing (thing_t* new_thing)
{
/* If queue is full, wait. */
while ( q_head + 16 == q_tail );
q[q_tail % 16] = new_thing;
q_tail = q_tail + 1;
}
q_head
q_tail
volatile

## Slide 7: Example of Synchronization (cont.)
Where should we add critical sections?
  none needed!
    no writes to the queues by both pieces of code
  but we do need to make q_head and q_tail volatile

## Slide 8: Example of Synchronization (cont.)
What about making program changes to make the code more compact?
  e.g., replace
q[q_tail % 16] = new_thing;
q_tail = q_tail + 1;
  with
q[(q_tail++) % 16] = new_thing;
Logically: they are equivalent sequential C code
However: Does store to q[..] or q_tail happen first?
Depends on the compiler’s constrains

## Slide 9: Multiprocessors and Locks
We solved the critical section problem for uniprocessors
What about multiprocessors?
  CLI … critical section …. STI
What is a multiprocessor?
  usually a symmetric multiprocessor (SMP)
  symmetric aspect: all processors have equal latency to all memory banks
  multicore processors are similar from our perspective
P
P
P
P
bus
I/O
I/O bus
M
M

## Slide 10: Multiprocessors and Locks (cont.)
Some non-uniform memory architecture (NUMA) machines were built
P
P
P
P
bus
I/O
I/O bus
M
M
com
P
P
P
P
bus
I/O
I/O bus
M
M
com

## Slide 11: Multiprocessors and Locks (cont.)
Multithreaded code is not protected by IF
Why haven’t we solved the atomicity problem on multiprocessors?
  interrupts are masked if IF is cleared!
  answer: IF is not cleared on other processors!
  just tell other processors to clear IF, too?
    too slow
    requires an interrupt!
We need to use shared memory to synchronize…

## Slide 12: Multiprocessors and Locks (cont.)
Logically, we use a lock
  when we want to access a piece of shared data we first look at the lock
  if it’s locked, we wait until it’s unlocked
  once it’s unlocked
    we lock it
    access the data
    then unlock it
shared
data
(locked state is
often represented
as 1)
shared
data
(unlocked state is
often represented
as 0)

## Slide 13: Multiprocessors and Locks (cont.)
Locking must be atomic with respect to other processors!
INCL (%EAX)
read EAX
add 1
put it back
P
P
M
read
write
It’s MY BUS!
LOCK: Prefix - execute following instruction with bus locked
LOCK INCL (%EAX)
Notes: X86 instructions are ATOMIC with respect to an interrupt/program on the same processor
Instructions executing on a given processor (P1) are not ATOMIC to an instruction stream which executes on another processor (P2) and which overlay with the initial stream on P1.

## Slide 14: Spin Locks
The simplest lock
  spin lock
  lock op
do {
try to change lock variable from 0 to 1
} while (attempt failed);
  other work to do? ignore it!
  spin in a tight loop on the lock (hence the name)
Once successful, program/interrupt handler owns the lock

## Slide 15: Spin Locks (cont.)
Only the owner can unlock
  How?
    (change lock variable to 0)
  Need to be atomic?
    (no, only owner can change when locked)
  What about memory op reordering?
    (must be avoided!)
Why keep asking the last question?
  reordering leads to subtle bugs
  unlikely to happen often
  unlikely to be repeatable
  very hard to find!

## Slide 16: Linux Spin Lock API
Static initialization
static spinlock_t a_lock = SPIN_LOCK_UNLOCKED;
Dynamic initialization
spin_lock_init (&a_lock);
When is dynamic initialization safe?
  lock must not be in use (race condition!)
  other synchronization method must prevent use

## Slide 17: Linux Spin Lock API – Basic Functions
void spin_lock (spinlock_t* lock);
void spin_unlock (spinlock_t* lock);

## Slide 18: Linux Spin Lock API – Testing Functions
int spin_is_locked (spinlock_t* lock);
returns 1 if held, 0 if not, but beware of races!
int spin_trylock (spinlock_t* lock);
make one attempt; returns 1 on success, 0 on failure
void spin_unlock_wait (spinlock_t* lock);
wait until available (race condition again!)

## Slide 19: Linux Spin Lock API (cont.)
Is spinlock enough to protect a critical section?
[let them try to come up with the problem]
what about
still need CLI/STI
which is first, CLI or lock? [ask]
  CLI first
  interrupt may occur between them, leading to second scenario above
P1
P2
try to get lock
(forced to wait)
interrupt (P2)
code
lock
gets lock
crit. sect.
unlock

## Slide 20: Linux Spin Lock API (cont.)
What about ?
Still need CLI/STI
Which is first, CLI or lock?
  CLI first
  interrupt may occur between them, leading to scenario above
P1
try to get lock
(waits forever!)
interrupt (P1)
code
lock
called a
deadlock

## Slide 21: Linux’ Lock/CLI Combo
static spinlock_t the_lock = SPIN_LOCK_UNLOCKED;
unsigned long flags;
spin_lock_irqsave (&the_lock, flags);
/* the critical section */
spin_unlock_irqrestore (&the_lock, flags);
asm volatile ("
PUSHFL
POPL %0
CLI
" : "=g" (flags) /* outputs */
: /* inputs */
: "memory" /* clobbers */
);
spin_lock (&the_lock);
Notes: Why FLAG ?
Compiler may not produce what you need , therefore you use embedded/inline asm
No portable
Preprocessor macro (parameterized d form of string replacement)
Any register
Memory can change
On uniprocessor this is NOP spinlock if you tell the kernel to compile for the uniprocessor
Unlock is not a macro
(Notice: Bit test and set (bts) alone does not guarantee the atomicity of the operation. )
Needs LOCK prefix
xchg is atomic i.e., it always asserts the LOCK signal regardless of the presence or absence of the LOCK prefix

## Slide 22: Linux’ Lock/CLI Combo (cont)
spin_unlock (&the_lock);
asm volatile ("
PUSHL %0
POPFL
" : /* outputs */
: "g" (flags) /* inputs */
: "memory", "cc" /* clobbers */
);

## Slide 23: Comments on code
Notice that spin_lock_irqsave changes the flags argument (it’s a macro)
The “memory” argument
  tells compiler that all memory is written by assembly block
  prevents compiler from moving memory ops across assembly
The “cc” argument
  condition codes change
  can lead to subtle bugs if left out!
spin_lock and spin_unlock calls
  become NOPs on uniprocessors
  in that case, calls just change IF
Restore rationale: may have had IF=0 on entry; if so, STI is unsafe

## Slide 24: Another Philosophy Lesson
Synchronization issues
  five hungry philosophers
  five chopsticks
Protocol
  take left chopstick (or wait)
  take right chopstick (or wait)
  eat
  release right chopstick
  release left chopstick
  digest
  repeat
  problems? deadlock!

## Slide 25: Another Philosophy Lesson (cont.)
How about the following protocol?
  take left chopstick (or wait)
  if right chopstick is free, take it
  else release left chopstick and start over
  eat
  release right
  release left
  digest
  repeat
Does this work?

## Slide 26: Another Philosophy Lesson (cont.)
What if all philosophers act in lock-step (same speed)?
left left left left left
release release release release release
left left left left left
release release release release release
left left left left left
(ad infinitum)
Called a livelock

## Slide 27: Another Philosophy Lesson (cont.)
To solve the problem, need (partial) lock ordering
  e.g., call chopsticks #1 through #5
  protocol: take lower-numbered, then take higher-numbered
  two philosophers try to get #1 first
  can’t form a loop of waiting philosophers
  thus someone will be able to eat
Notes: Do need to compare any two lock
Any required by a give piece of code

## Slide 28: Example of Code Understanding
Given code in left column
  Which other columns are compatible (i.e., can’t lead to deadlock)?
#0 #1 #2 #3
lock A lock B
lock B lock A lock A lock B
. . . .
. . . .
. . . .
unlock B unlock A unlock A unlock B
unlock A unlock B
  Columns 2 and 3 are compatible with column 0
Notes: Lockirq a
Lock B lockirqsave
Unlock B
Critical section in an interupt
Programio control
No critical section in an interrrupt handler
unlockA
Save site is to use irqsave
IF 0
IF+1

## Slide 29: Conservative Synchronization Design
Getting synchronization correct can be hard
  it’s the focus of several research communities
On uniprocessor
  mentally insert handler code between every pair of adjacent instructions
  ask whether anything bad can happen
  if so, prevent with CLI/STI

## Slide 30: Conservative Synchronization Design (cont)
On a multiprocessor
  consider all possible interleavings of instructions
  amongst all pieces of (possibly concurrent) code
  ask whether anything bad can happen
  if so, use a lock to force serialization
  good luck!

## Slide 31: Conservative Synchronization Design (cont)
What does “bad” mean, anyway?
A conservative but systematic definition
  if any data written by one piece of code
  are also read or written by another piece of code
  these two pieces must be atomic with respect to each other

## Slide 32: Conservative Synchronization Design (cont)
Consider the following two pieces of code…
write X write Q
read A read A
compare A, 4 read B
jne target multiply A by B
read B write A
add 1 to B read R
write B write S
target: read Y
read B
write Z
not shared
not shared
not shared
not shared
not shared
reading B is not a conflict
Methodology courtesy of
Andrew Chien’s Concert work in 90s]
Notes: Ignore the parts that do not touch shared data

## Slide 33: Conservative Synchronization Design (cont)
What variables are shared? [A and B]
step 0: ignore the parts that don’t touch shared data
step 1: calculate read & write sets
A: read A: read & written
B: read & written B: read
step 2: check for R/W, W/W relationships
  A written by right side, read by left
  B written by left side, read by right
  must be atomic!
step 3: add lock(s) to guarantee atomic execution (pick order if > 1 locks)
step 4: optimize if desired
not shared