## Slide 1: ECE391 Computer System Engineering Lecture 9
Dr. Zbigniew Kalbarczyk
University of Illinois at Urbana- Champaign
Spring 2014

## Slide 2: Lecture Topics
Selecting synchronization mechanisms
Programmable interrupt controller (PIC)
  motivation & design
  hardware for x86
  Linux abstraction of PIC

## Slide 3: Aministrivia
Midterm Exam1
  February 27, 7:00pm
  Please notify us about any conflict by
  5:00pm Friday, February 21
Review Session
  Thursday February 27 IN CLASS

## Slide 4: Selecting a Synchronization Mechanism (cont)
Safe selection (when in doubt…)
 | mutual exclusion | reader/writer
data shared by interrupt handlers | spin_lock_irqsave spin_unlock_irqrestore | read/write__lock_irqsave read/write_unlock_irqrestore
data shared only by system calls | down up | down_read/write up_read/write
Notes: Examples

## Slide 5: Synch. Selection Example from RTC Driver
Interrupt handler
  increment count atomically
  read device & replace bottom byte
Code (file read system call)
  read data
  reset data to 0
  atomic with respect to interrupt handler
# interrupts
since last read
shared data (4B)
type of last
interrupt

## Slide 6: Synch. Selection Example from RTC Driver (cont)
Interrupt handler code
spin_lock (&rtc_lock);
data += 0x100;
data &= ~0xFF;
data |= (flag_port_read () & 0xF0);
spin_unlock (&rtc_lock);
Why not _irq? _irqsave?
  code only executes in interrupt handler
  never interrupts itself

## Slide 7: Synch. Selection Example from RTC Driver (cont.)
File read system call
spin_lock_irq (&rtc_lock);
tmp = data;
data = 0;
spin_unlock_irq (&rtc_lock);
Why _irq? why not _irqsave?
  code only executes in system call
  interrupts always enabled on entry (safe to do STI at end)

## Slide 8: PIC Motivation and Design
How do we connect devices to the processor’s interrupt input?
An OR gate? why not?
  who writes the vector # ?
    possible to build arbiter, but…
    what if more than one raised interrupt?
  extra work for processor to query all devices
    must execute interrupt code for device that raised interrupt
    could have been more than one device
    no way to tell with OR gate
INTR
8
(INTA)’
x86
D
many
devices
which
interrupt?
Notes: PIC motivation & design
Hardware for x 86

## Slide 9: PIC Motivation and Design (cont.)
  not all devices support query
    many devices too simplistic to support query
    and operations (e.g., reading from port) may not be idempotent
  nice to have concept of priority and preemption, i.e., interrupting an interrupt handler

## Slide 10: 8259A Programmable Interrupt Controller (PIC)

## Slide 11: Logical Model of PIC Behavior
Watch for interrupt signals
  from up to eight devices
  one interrupt line each
Using internal state
  track which devices/input lines
  are currently in service by processor
  i.e., processor is executing interrupt handler for that interrupt

## Slide 12: Logical Model of PIC Behavior (cont)
When a device raises an interrupt
  check if priority is higher than those of in-service interrupts
  if not, do nothing
  if so
    report the highest-priority raised to the processor
    mark that device as being in service

## Slide 13: Logical Model of PIC Behavior (cont.)
When processor reports EOI (end of interrupt) for some interrupt
  remove the interrupt from the in-service mask
  check for raised interrupt lines
    that should be reported to processor

## Slide 14: Logical Model of PIC Behavior (cont.)
Protocol for reporting interrupts
  PIC raises INTR
  processor strobes INTA’ (active low) repeatedly
    creates cycles for PIC to write vector to data bus
    (must follow spec timing! PIC is not infinitely fast!)
  processor sends EOI with specific combinations of A & D inputs (A is from address bus, D is from data bus)
Notes: If IF = 0 CPU will ignore INTR
PIC uses logical clock signal to send data to the processor
Data bus is memory would use same which the data lines that memory would use
Generate a and D to dosr ore and In and out

## Slide 15: Logical Model of PIC Behavior (cont.)
What about A, CS’, RD’, and WR’ ?
  A = address match for ports
  CS’ = chip select (does processor want PIC to read/write?)
  RD’ and WR’ defined from processor’s point of view
    RD’ = processor will read data (vector #) from PIC
    WR’ = processor will write data (command, EOI) to PIC
Notes: A says which port
CS’ acitve low
Two ports on the PIC only when those are invoke we pay attention

## Slide 16: Logical Model of PIC Behavior (cont.)
Map to ports 0x20 & 0x21
  given ADDR bus
  logic to form A and CS’ inputs to PIC
Remember
  the PIC is asynchronous!
  all interactions have timing constraints
  see specifications for details
to A on PIC
ADDR bus
to CS’
15
≠ 0x10
ADDR[0]
ADDR[15:1]
Notes: Historically port for master are at 20 and 21 hex
Original design there was glue logic A&CS’
ADDR[0]
ADDR[[15:1]
Add comparator
PIC is asynchronous INTR is not aligned with CPU clock

## Slide 17: Logical Model of PIC Behavior (cont.)
What about SP’ & CAS?
Are eight devices enough? No? What then?
  hook 2, 3, or 4 PICs to processor?
  [same problem as before!]
  design a big PIC?
  [waste of transistors; not cheap in 8259A era]
  design several PICs?
  [waste of humans! (and production costs)]
Better answer: cascade
master
slave
slave
. . .
devices (up to 64)
up to 8
slaves
1 master
Notes: Are 8 devices enough?
WE want to have more than 8 many hard drive; many usb
Dial-up lines multiple modems in the server
Who is going to run the INTR
Rather than OR gate use another PIC
PIC can operate as master or slave

## Slide 18: Cascade Configuration of PICs
Notes: Both on the data bus
Same INTA
Master drives INTR
WHo writes the vector # to the processor

## Slide 19: Cascade Configuration of PICs (cont)
Both PICs on bus
Both see INTA’
INT from slave goes to IR2 on master
M/S chosen using SP’ input
All done? Who writes the vector # ?
  slave can’t know if its priority is highest
  master doesn’t know which of slave’s interrupts was high
  solution: cascade bus
  master writes its own vector # ‘s
  or writes slave’s identification number to CAS bus to tell slave to write vector #
Notes: Either chips needs to write the Data bus
Solution is a CAS bus
In line 2 master writes 2 on the CAS bus to tel slave to write to Data if slave sees the 2 on CAS it knows to drive the data bus

## Slide 20: PIC (cont.)
8259A also supports many unmentioned features (the programmable part)
  example: vector #
    three low bits taken from IR line #
    five high bits are programmable (set by software)
  bit vector (more internal state) to mask individual interrupts
  multiple ISAs supported ………
Why consider 8259A?
  originally a separate chip
  later integrated into chipset
  latest Intel processors integrate (emulation of) 8259 onto chip
Notes: NMI can be masked by PIC

## Slide 21: PIC (cont.)
Previous figure showed x86 configuration of two 8259A’s
  master 8259A mapped to ports 0x20 & 0x21
  slave 8259A mapped to ports 0xA0 & 0xA1
  slave connects to IR2 on master
Question
  prioritization on 8259A: 0 is high, 7 is low
  what is prioritization across all 15 pins in x86 layout?
  (highest) M0…M1…S0…S7…M3…M7 (lowest)

## Slide 22: PIC (cont.)
In Linux (initialization code to be seen shortly)
  master IR’s mapped to vector #’s 0x20 – 0x27
  slave IR’s mapped to vector #’s 0x28 – 0x2F
  remember the IDT?

## Slide 23: Interrupt Descriptor Table
Notes: IDT
X86 init code puts the intrrupts into for slave and
Setting by high 5 bit of int vector

## Slide 24: Linux 8259A Initialization
Notes: Init happens early in the
The memory is later reclaim
Power cycle may need to be initialize
auto_eoi a lot of is 2.4 scheduler is 2.6
CPU automatically does the init
Is o for now
Blocking the ints for safety
Turning off the interrupt in different way
IF is disable
Out_b macro to send byte to th eprot
Adds the puse instruction to met the speed of the PIC
Get initialize do not generate interrupts
No other CPUs recive interrupts

## Slide 25: Comments on Linux’ 8259A Initialization Code
What is the auto_eoi parameter? always = 0
Four initialization control words to set up the master 8259A
Four initialization control words to set up the slave 8259A
port(A=?) info contained in Initialization Control Word
ICW1 0 start init, edge-triggered inputs, cascade mode, 4 ICWs
ICW2 1 high bits of vector #
ICW3 1 master: bit vector of slaves; slave: input pin on master
ICW4 1 ISA=x86, normal/auto EOI
Notes: Initialization contorl word
… tell the mster to connect a slev; Four control words, different ways of initialization; not level trigger, PIC treast transition o to 1 to indicate INTR
Go to port to 21 low bits are not use here 0010 o for the master slave 0010 1 for slave
Go to port 1 PIC know how to intrpret them
X86tells the protocol to use;
People did not worry before the PIC is initialize
Do not generate int if there is no code to handle
First init and than the PIC know which device to serve when you register the device

## Slide 26: Comments on Linux’ 8259A Initialization Code (cont.)
What does the “_p” mean on the “outb” macros?
  add PAUSE instruction after OUTB; “REP NOP” prior to P4
  delay needed for old devices that cannot handle processor’s output rate
Critical section spans the whole function; why?
  avoid other 8259A interactions during initialization sequence
  (device protocol requires that four words be sent in order)
Why use _irqsave for critical section?
  this code called from other interrupt initialization routines
  which may or may not have cleared IF on processor